## Slide 1: CSE 390 Advanced Computer Networking
Lecture 3: Internet Architecture
(Layer cake and an hourglass)
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 2: Last time …
History + Introduction
… Today: architecture, physical, + data link layer

## Slide 3: Goals of the Internet Architecture (Clark ‘88)
Connect existing networks
Robust in face of failures (not nuclear war…)
Support multiple types of services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability
Notes: Different types of services: e.g., even those that don’t want TCP (network debugging)
Cost effective: efficiently use the expensive communication resource. -> 40 B header “long”
Accountability becomes more important as non-military folks start to use the network

## Slide 4: Robust
As long as the network is not partitioned, two endpoints should be able to communicate
Failures (excepting network partition) should not interfere with endpoint semantics (why?)
Maintain state only at end-points
  Fate-sharing, eliminates network state restoration
    If information associated with an entity is lost, then the entity itself must have been lost
  stateless network architecture (no per-flow state)
Routing state is held by network (why?)
No failure information is given to ends (why?)

## Slide 5: Types of Services
Use of the term “communication services” already implied that they wanted application-neutral network
Realized TCP wasn’t needed (or wanted) by some applications
Separated TCP from IP, and introduced UDP
  What’s missing from UDP?
Notes: Network debugging application  used when network is performing poorly will take what it can get. XNET

## Slide 6: Variety of Networks
Incredibly successful!
  Minimal requirements on networks
  No need for reliability, in-order, fixed size packets, etc.
IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: ATM, SONET, WDM…

## Slide 7: Host Attachment
Clark observes that the cost of host attachment may be somewhat higher because hosts have to be smart
  Imagine a time before all that functionality existed in the OS!
But the administrative cost of adding hosts is very low, which is probably more important
  Happens within a logical domain, no need to coordinate with others

## Slide 8: Real Goals
Something that works…..
Connect existing networks
Survivability (not nuclear war…)
Support multiple types of services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 9: Internet Motto
We reject kings , presidents, and voting.
We believe in rough consensus and running code.”
David Clark

## Slide 10: Questions
What priority order would a commercial design have?
What would a commercially invented Internet look like?
What goals are missing from this list?
Which goals led to the success of the Internet?
Something that works…..
Connect existing networks
Survivability (not nuclear war…)
Support multiple types of services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability
Notes: Missing: resource sharing, other considerations of malicious users (traceback, etc.), address concerns of administrative domains visible

## Slide 11: Organizing Network Functionality
Networks are built from many components
  Networking technologies
    Ethernet, Wifi, Bluetooth, Fiber Optic, Cable Modem, DSL
  Network styles
    Circuit switch, packet switch
    Wired, Wireless, Optical, Satellite
  Applications
    Email, Web (HTTP), FTP, BitTorrent, VoIP
How do we make all this stuff work together?!

## Slide 12: Problem Scenario
Web
Email
Bittorrent
Ethernet
802.11
Bluetooth
VoIP
Cellular
This is a nightmare scenario
Huge amounts of work to add new apps or media
Limits growth and adoption

## Slide 13: More Problems
Bittorrent
Ethernet
802.11
Bittorrent
Application endpoints may not be on the same media

## Slide 14: Solution: Use Indirection
Web
Email
Bittorrent
Ethernet
802.11
Bluetooth
VoIP
Cellular
Magical Network Abstraction Layer
O(1) work to add new apps, media
Few limits on new technology
API
API
API
API

## Slide 15: Layered Network Stack
Modularity
  Does not specify an implementation
  Instead, tells us how to organize functionality
Encapsulation
  Interfaces define cross-layer interaction
  Layers only rely on those below them
Flexibility
  Reuse of code across the network
  Module implementations may change
Unfortunately, there are tradeoffs
  Interfaces hide information
  As we will see, may hurt performance…
Applications
Physical
Media
Layer N
Layer 1
Layer 2
…

## Slide 16: Key Questions
How do we divide functionality into layers?
  Routing
  Congestion control
  Error checking
How do we distribute functionality across devices?
  Example: who is responsible for security?
Switch
Switch
Router
  Security
  Fairness
  And many more…

## Slide 17: Outline
Layering
  The OSI Model
Communicating
  The End-to-End Argument

## Slide 18: The ISO OSI Model
OSI: Open Systems Interconnect Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Switch
Host 2
Physical
All devices implement the first three layers
Layers communicate peer-to-peer
Layers communicate peer-to-peer

## Slide 19: Layer Features
Service
  What does this layer do?
Interface
  How do you access this layer?
Protocol
  How is this layer implemented?
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 20: Physical Layer
Service
  Move information between two systems connected by a physical link
Interface
  Specifies how to send one bit
Protocol
  Encoding scheme for one bit
  Voltage levels
  Timing of signals
Examples: coaxial cable, fiber optics, radio frequency transmitters
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 21: Data Link Layer
Service
  Data framing: boundaries between packets
  Media access control (MAC)
  Per-hop reliability and flow-control
Interface
  Send one packet between two hosts connected to the same media
Protocol
  Physical addressing (e.g. MAC address)
Examples: Ethernet, Wifi, DOCSIS
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 22: Network Layer
Service
  Deliver packets across the network
  Handle fragmentation/reassembly
  Packet scheduling
  Buffer management
Interface
  Send one packet to a specific destination
Protocol
  Define globally unique addresses
  Maintain routing tables
Example: Internet Protocol (IP), IPv6
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 23: Transport Layer
Service
  Multiplexing/demultiplexing
  Congestion control
  Reliable, in-order delivery
Interface
  Send message to a destination
Protocol
  Port numbers
  Reliability/error correction
  Flow-control information
Examples: UDP, TCP
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 24: Session Layer
Service
  Access management
  Synchronization
Interface
  It depends…
Protocol
  Token management
  Insert checkpoints
Examples: none
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 25: Presentation Layer
Service
  Convert data between different representations
  E.g. big endian to little endian
  E.g. Ascii to Unicode
Interface
  It depends…
Protocol
  Define data formats
  Apply transformation rules
Examples: none
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 26: Application Layer
Service
  Whatever you want :)
Interface
  Whatever you want :D
Protocol
  Whatever you want ;)
Examples: turn on your smartphone and look at the list of apps
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 27: Encapsulation
How does data move through the layers?
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data
Data

## Slide 28: Real Life Analogy
Postal Service
Label contains routing info
Un-packing
Doesn’t know contents of letter
Doesn’t know how the Postal network works

## Slide 29: Network Stack in Practice
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Switch
Host 2
Physical
Video Client
UDP
Video Server
UDP
FTP Client
TCP
IP
Ethernet
IP
Ethernet
FTP Server
TCP
IP
Ethernet
802.11n
802.11n
802.11n

## Slide 30: Encapsulation, Revisited
Web Server
TCP
IP
Ethernet
HTTP Header
TCP Header
IP Header
Ethernet Header
Ethernet Trailer
Web Page
HTTP Header
Web Page
TCP Header
HTTP Header
Web Page
IP Header
TCP Header
HTTP Header
Web Page
TCP Segment
IP Datagram
Ethernet Frame

## Slide 31: The Hourglass
IPv4
TCP, UDP, ICMP
HTTP, FTP, RTP, IMAP, Jabber, …
Ethernet, 802.11x, DOCSIS, …
Fiber, Coax, Twisted Pair, Radio, …
One Internet layer means all networks interoperate
All applications function on all networks
Room for development above and below IP
But, changing IP is insanely hard
Think about the difficulty of deploying IPv6…

## Slide 32: Orthogonal Planes
Application
Presentation
Session
Transport
IP
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Well cover this later…
Control plane: How Internet paths are established

## Slide 33: Orthogonal Planes
Application
Transport
Network
Data Link
Network
Data Link
Host 1
Switch(es)
Host 2
Application
Transport
Network
Data Link
Data plane: How data is forwarded over Internet paths

## Slide 34: Reality Check
The layered abstraction is very nice
Does it hold in reality?
No.
Firewalls
Analyze application layer headers
Transparent Proxies
Simulate application endpoints within the network
NATs
Break end-to-end network reachability

## Slide 35: Outline
Layering
  The OSI Model
Communicating
  The End-to-End Argument

## Slide 36: From Layers to Eating Cake
IP gives us best-effort datagram forwarding
  So simple anyone can do it
  Large part of why the Internet has succeeded
  …but it sure isn’t giving us much
Layers give us a way to compose functionality
  Example: HTTP over TCP for Web browsers with reliable connections
…but they do not tell us where (in the network) to implement the functionality

## Slide 37: Where to Place Functionality
How do we distribute functionality across devices?
  Example: who is responsible for security?
Switch
Switch
Router
?
?
?
?
?
“The End-to-End Arguments in System Design”
  Saltzer, Reed, and Clark
  The Sacred Text of the Internet
  Endlessly debated by researchers and engineers

## Slide 38: Basic Observation
Some applications have end-to-end requirements
  Security, reliability, etc.
Implementing this stuff inside the network is hard
  Every step along the way must be fail-proof
  Different applications have different needs
End hosts…
  Can’t depend on the network
  Can satisfy these requirements without network level support

## Slide 39: Example: Reliable File Transfer
Solution 1: Make the network reliable
Solution 2: App level, end-to-end check, retry on failure
Integrity Check
Integrity Check
Integrity Check
App has to do a check anyway!

## Slide 40: Example: Reliable File Transfer
Solution 1: Make the network reliable
Solution 2: App level, end-to-end check, retry on failure
Please Retry
Full functionality can be built at App level
In-network implementation…
  Doesn’t reduce host complexity
  Does increase network complexity
  Increased overhead for apps that don’t need functionality
But, in-network performance may be better

## Slide 41: Conservative Interpretation
“Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level” (Peterson and Davie)
Basically, unless you can completely remove the burden from end hosts, don’t bother

## Slide 42: Radical Interpretation
Don’t implement anything in the network that can be implemented correctly by the hosts
Make network layer absolutely minimal
Ignore performance issues

## Slide 43: Moderate Interpretation
Think twice before implementing functionality in the network
If hosts can implement functionality correctly, implement it a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality…
…and if it doesn’t cost too much $ to implement

## Slide 44: Reality Check, Again
Layering and E2E principals regularly violated
Firewalls
Transparent Proxies
NATs
Conflicting interests
  Architectural purity
  Commercial necessity

## Slide 45: Takeaways
Layering for network functions
  Helps manage diversity in computer networks
  Not optimal for everything, but simple and flexible
Narrow waist ensures interoperability, enables innovation
E2E argument (attempts) to keep IP layer simple
Think carefully when adding functionality into the network