## Slide 1: CSE390 Advanced Computer Networks
Lecture 17: Internet Censorship
(Roadblocks on the information superhighway …)
Based on slides by N. Weaver. Updated by P Gill. Fall 2014

## Slide 2: What is censorship?
Censorship, the suppression of words, images, or ideas that are "offensive," happens
whenever some people succeed in imposing their personal political or moral values on others.
Censorship can be carried out by the government as well as private pressure groups. Censorship by the government is unconstitutional.
– The American Civil Liberties Union

## Slide 3: What is censorship?
Key points:
Censorship in general is a non-technical problem
  Think banned books, suppression of news media etc.
In the United States censorship is unconstitutional
  Other countries?
  Are we forcing Western values on other countries?
  United Nations Universal Declaration of Human Rights provides some guidance of what speech should be protected globally
    E.g., political, minority religions, LGBT, etc.

## Slide 4: What is a network censor
An entity that desires that some identifiable communication is blocked from being transmitted over the network
Without the authority to compel the content provider to remove the content
Without the authority to compel the client to install software of the censor’s choosing
Requires that the censor act on network traffic
Image from Watch, Learn, Drive
http://watch-learn-drive.com/Learners_Online/New_places/Traffic_lights/TL_5.html
Notes: Needs to operate on network traffic. Needs to be efficient and scalable. Censorship systems are like other systems!

## Slide 5: How to identify and block?
Identification: The piece of information that allows the censor to identify content to be blocked is referred to as the censorship trigger
  Example: IP address, hostname, URL, keywords etc.
Blocking: The technical means used to restrict access to the content
  Example: dropping packets, forging TCP RST packets or DNS responses
In the next few slides we will be exploring censorship as it exploits different triggers and blocking mechanisms at different layers of the Internet Protocol stack.

## Slide 6: Networking 101
Protocols on the Internet divided into logical layers
These layers work together to get traffic where it is going.
Headers of upper layers encapsulate lower layer protocols
A network censor can disrupt any layer!
Application layer
(DNS, HTTP, HTTPS)
Transport Layer
(TCP, UDP)
Network Layer
(IP, ICMP)
Link Layer
(Ethernet, 802.11)
Physical Layer
(satellite, fiber)
Bit Torrent, Web (Facebook, Twitter)

## Slide 7: Networking 101
So how does our traffic get where its going?
DNS Server
(2.1.2.3)
Web Server
(3.1.2.3)
Home connection
(2.1.2.4)
Each device has an IP
Within a network routes are learned via “interior gateway protocols” (e.g., OSPF, IS-IS )
ISP B
ISP A
ISP C
Between networks border gateway protocol (BGP) is used to exchange routes
C
Prefix: 3.1.2.0/24
C
Prefix: 3.1.2.0/24
B, C
Prefix: 3.1.2.0/24
(2.1.2.5)
2.1.2.5
Prefix: 3.1.2.0/24
Notes: Unhide for SysSec class.
When the user wants to access the Web server they learn the path via BGP.

## Slide 8: Networking 101
…ok but humans don’t request IP addresses
… they want content!
DNS Server
(2.1.2.3)
Web Server
(208.80.154.238)
Home connection
(2.1.2.4)
ISP B
ISP A
ISP C
(2.1.2.5)
DNS QTYPE A
En.wikipedia.org
DNS A
208.80.154.238
SYN
ACK
SYNACK
HTTP GET /wiki/Douglas_MacArthur HTTP 1.1
Host: en.wikipedia.org
HTTP STATUS 200
Content Length: 523
Content Type: text/html
<!DOCTYPE html>
<html lang="en" dir="ltr" class="client-nojs">
<head>
<meta charset="UTF-8" /><title>Douglas MacArthur - Wikipedia, the free encyclopedia</title>
<meta name="generator" content="MediaWiki 1.23wmf10" />

## Slide 9: Many opportunities to censor
Block IP addresses
  IP layer
Block hostnames
  DNS (application layer)
Disrupt TCP flows
  TCP (transport layer)
  Many possible triggers
Disrupt HTTP transfers
  HTTP (application layer)

## Slide 10: Internet protocol 101
Relevant fields:
IPID: set by the sender of the IP packet. Some OSes increment globally for each IP packet generated by the host; some maintain per flow counters, use a constant or random values.
TTL: counter gets decremented by each hop on the path until it reaches 0 and an ICMP Time Exceeded Message is generated. Useful for probing/locating censors.
Source IP: IP of the sender of this packet
Destination IP: IP of the recipient of this packet

## Slide 11: IP-based blocking
Option 1: Configure routers using an access control list (ACL) to drop traffic to a given IP address.
Drop traffic to:
8.7.198.45
203.98.7.65
46.82.174.68
59.24.3.173
93.46.8.89
Image from Watch, Learn, Drive
http://watch-learn-drive.com/Learners_Online/New_places/Traffic_lights/TL_5.html
Source: 136.159.220.20
Destination: 46.82.174.68
This is an example of in-path blocking
(censor can remove packets)

## Slide 12: IP-based blocking
Option 1: Configure routers using an access control list (ACL) to drop traffic to a given IP address.
Drop traffic to:
8.7.198.45
203.98.7.65
46.82.174.68
59.24.3.173
93.46.8.89
Image from Watch, Learn, Drive
http://watch-learn-drive.com/Learners_Online/New_places/Traffic_lights/TL_5.html
Source: 136.159.220.20
Destination: 46.82.174.70

## Slide 13: IP-Based blocking
Advantages (for the censor)
  Quick and easy to configure
  Routers have efficient techniques for IP matching
Disadvantages
  Need to know the IP
    Easily evadable!
  High collateral damage: IP != Web host
    Noticeable if high profile site is hosted on the same system
    60% of Web servers are hosted with 10,000 or more other Web servers (Shue et al. 2007)
  Location of the censor can be determined from within the censored network
    Just need to traceroute to the blocked IP (use TCP port 80 SYNs in case ACL is selective).
  Can determine location from censored host as well
    Assuming ICMP Time Expired messages are blocked.

## Slide 14: IP-BASED BLOCKING
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
Option 2: Use BGP to block IPs
  February 2008 : Pakistan Telecom hijacks YouTube
Notes: -level of autonomous systems
-e.g., YouTube, AT&T, pakistan telecom
-routing is done on IP addresses, so when someone wants to go to YouTube they get YouTube’s IP address and YouTube announces to the world that they have the ip address and traffic is forwarded towards them. So here multinet would route to it’s provider pakistan telecom that then forwards the traffic on to youtube.
-these networks chosen for a specific reason which is that there was an incident in february 2008 pakistan telecom actually high jacked traffic going to youtube (misconfiguration).
-they announced to the world that they’re youtube and traffic destined to youtube was routed to them
-youtube was unavailable for a couple of hours as operators phone each other to figure out what was going on.

## Slide 15: IP-BASED BLOCKING
  Here’s what should have happened….
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
X
Hijack + drop packets going to YouTube
  Block your own customers.

## Slide 16: IP-BASED BLOCKING
  But here’s what Pakistan ended up doing…
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
Pakistan
Telecom
No, I’m YouTube!
IP 208.65.153.0 / 24
Notes: Our works focuses on attacks of this flavor..

## Slide 17: Why was the Pakistan incident so bad?
They announced a more specific prefix
  BGP routing is based on longest prefix match
There is no global route authentication in place!
  ISPs should filter announcements from their customers that are clearly wrong
  (As an ISP you should know what IP address space is in use by your customers)
  In reality this is harder than it seems 

## Slide 18: Ip-based blocking
Option 2: BGP route poisoning
Instead of configuring router ACLs, just advertise a bogus route
  Causes routers close to the censor to route traffic to the censor, which just drops the traffic
How to detect this type of censorship?
  BGP looking glass servers in the impacted region
  Sometimes global monitors as well …
Challenges
  Can cause international collateral damage!
  Will block all content on a given prefix
    Could announce a /32 to get a single address but most ISPs will not propagate beyond a /24

## Slide 19: Known users of ip-based blocking
Pakistan using IP-based blocking for YouTube address ranges
  Can interfere with other Google services
China
  Some reports of IP blocking
  Many URLs redirected to small set of IP-addresses, possibly this is the set used for ACLs
UK
  Uses IP blocking of the Pirate Bay’s IP address
Australia
  IP blocking for Melbourne Free University IPs (precise motivation unclear…)
  https://www.eff.org/deeplinks/2013/04/australian-networks-censor-community-education-site
In general, too much collateral damage of IP-based blocking.

## Slide 20: Overview
Block IP addresses
  IP layer
Disrupt TCP flows
  TCP (transport layer)
  Many possible triggers
Block hostnames
  DNS (application layer)
Disrupt HTTP transfers
  HTTP (application layer)

## Slide 21: Tcp: Transmission control protocol
TCP is used for reliable, in-order communication
Connection established using a “three-way handshake”
All data is ACKnowledged
  If no ACK is received packets will be resent
Connection normally closed with a FIN (finish) packet
  Indicates that this side has no more information to send
Connections can also be closed with a RST (reset) packet
  Indicates a problem: both sides should stop communicating
  Some software makes liberal use of RSTs.

## Slide 22: Why inject tcp reset packets?
A TCP Reset (RST) tells the other side of the connection:
  There will be no more data from this source on this connection
  This source will not accept any more data, so no more data should be sent
Once a side has decided to abort the connection, the only subsequent packets sent on this connection may be RSTs in response to data.
Once a side accepts a RST it will treat the connection as aborted
… but RSTs are quite common, 10-15% of ALL flows are terminated by a RST rather than a FIN
  For HTTP, it can be over 20%: Web servers/browsers often time out with RST instead of FIN
  Thus we cannot treat RSTs as “adversarial”

## Slide 23: types of censors
Last time we discussed IP blocking via ACLs which is an example of an in-path censor.
Censors can also operate on-path: a wiretap, (intrusion detection system (IDS), deep packet inspection (DPI)) + attached network connection
  Censor can see all the packets
  Censor can add their own packets through packet injection
  Censor cannot remove packets
Can censor:
  DNS requests (by injecting bogus replies)
  Web requests to given hosts (including HTTPS)
  Web requests over HTTP for forbidden content
    Latter two possible via injecting TCP RST packets!

## Slide 24: Limitations of on-path censors

## Slide 25: Why on-path censors?
In-path device must process the traffic
  If they fail, they fail closed (connection gone!)
On-path devices are safer
  Tapping a link is “safe” (in network operator terms)
  Easy to parallelize (just mirror traffic to more filters)
  Less disruptive to install and use
Limitations:
  Can’t censor single replies
  Censorship is always detectable
    Censor cannot perfectly mimic the other endpoint.

## Slide 26: On path censor example
Notes: Mirroring is only on the active link. If that link goes down traffic on back up link may not be censored.

## Slide 27: Detecting on-path censorship
Not only is the act of censorship detectable, the mechanism, is detectable
Since censor creates new packets but can’t remove existing packets
Since the injected packets can be identified, fingerprinting is also possible.
Using packets which trigger censorship but with a short TTL can localize the censor in the network
Leads to tricky cross-layer network measurements (easier with DNS)
Detection limitation: Can only detect an on-path censor when it is active
A censor which doesn’t create an effect on measured traffic is not detectable
E.g., DPI used for surveillance

## Slide 28: Race conditions: data after reset
TCP packets are tracked by sequence numbers
  The next packet’s sequence number should be the previous packet’s sequence number plus the packet length
What is a sender is still sending data when the RST is injected?
  The receiver will see both a reset and a subsequent data packet, where the packet’s sequence number + length > the reset packet’s sequence number

## Slide 29: Race conditions: Data after reset
Web Server
(208.80.154.238)
Data seq = 32 ack = 1
RST seq = 2 ack = 32
Data seq = 238 ack = 32
Data after RST? Doesn’t make sense!
Such a packet arrangement is out of specification
No TCP stack should generate such a sequence! It would imply that the stack decided to abort the connection yet keep sending anyway

## Slide 30: Race conditions: reset after data
What if the reset injector is just slow?
  It takes time to determine that a flow should be blocked…
  … in the mean time traffic is flying by!
Result is a reset after data race condition
  Reset packet appears after the data packet
  Reset’s sequence number is less than the data packet’s sequence number plus its length

## Slide 31: Race conditions: Reset after data
Web Server
(208.80.154.238)
Data seq = 32 ack = 1
RST seq = 2 ack = 32
Data seq = 238 ack = 32
RST after data? Huh?
This is also out of specification
Why would a TCP stack do a retroactive abort?
Worse, such resets should be ignored by the receiver:
The received reset is “out-of-window”

## Slide 32: Building a reliable RST injector enables detection
Thus a reliable packet injector must anticipate the reset after data condition
  Instead of sending one reset it needs to send multiple resets with increasing sequence number
This is detectable as a “reset sequence change condition”
  An end host should never generate such resets as the host can always generate an in-sequence reset
An unreliable injector can only be detected when a race condition occurs
A reliable injector always can be detected.

## Slide 33: Fingerprinting rst injectors

## Slide 34: Can we just ignore these RSTs?
As of 2006, yes but both ends of the connection need to ignore the RSTs.
Client cannot do it unilaterally.
  Injectors will just send RSTs to the server and the client

## Slide 35: Remember … RSTs are a mechanism
They don’t tell us anything about what triggers the mechanism
Some clues ..
  When the RST is sent
    Before the HTTP GET
    After the HTTP GET
  Still not definitive
Need purpose build experiments
  Run tests towards your own server
  Put blocked keyword in host name
  … in HTML body content

## Slide 36: Overview
Block IP addresses
  IP layer
Disrupt TCP flows
  TCP (transport layer)
  Many possible triggers
Block hostnames
  DNS (application layer)
Disrupt HTTP transfers
  HTTP (application layer)

## Slide 37: Domain name system (dns)

## Slide 38: How can we block DNS?
A few things to keep in mind …
No cryptographic integrity of DNS messages
  DNSSEC proposed but not widely implemented
Caching of replies means leakage of bad DNS data can persist

## Slide 39: Blocking dns names

## Slide 40: Blocking dns names

## Slide 41: Blocking DNS names
Option A: get ISP resolver on board
  (Previous slide)
Option B: On-path packet injection similar to TCP Resets
  Can be mostly countered with DNS-hold-open:
    Don’t take the first answer but instead wait for up to a second
  Generally reliable when using an out of country recursive resolve
    E.g., 8.8.8.8
  Can be completely countered by DNS-hold-open + DNSSEC
    Accept the first DNS reply which validates

## Slide 42: Hold-on in action

## Slide 43: Checking feasibility: RTT

## Slide 44: Checking feasibility: ttl

## Slide 45: Performance of Hold-on
Lesson: You don’t have to wait that long to get the legitimate reply
Notes: Potential project, create a browser plug in that implements hold-on.

## Slide 46: Overview
Block IP addresses
  IP layer
Disrupt TCP flows
  TCP (transport layer)
  Many possible triggers
Block hostnames
  DNS (application layer)
Disrupt HTTP transfers
  HTTP (application layer)

## Slide 47: Networking 101: HTTP
HTTP (Hyper Text Transfer Protocol) is what most people think of when they talk about “the web”
Client-server request/response protocol
  Client requests “I want file X from host Y that is on this server”
  Server replies
Content can be any filetype
E.g. “HyperText Markup Language” (HTML) pages
  Embedded programs (JavaScript, Flash, etc) which run on the browser
No cryptographic integrity

## Slide 48: HTTPS ADDS ENCRYPTION
The TLS (Transport Layer Security) protocol
  Sits “between” TCP and HTTP
Uses cryptographic certificates to authenticate the server
  One of ~300 entities vouch for (or vouch for someone who vouches for) the server
    Who do you trust? CNNIC? US DOD? Your browser trusts them...
    These days, however, fake certs get noticed: Certificate pinning in Google Chrome, certificate observatories and notaries, etc...
Without a fake certificate, the data is cryptographically protected
  But does not protect the TCP control messages
  And does not protect against traffic analysis: Certificate effectively asserts what is the hostname! Also watching dataflow can often infer content

## Slide 49: OK … SO WHERE ARE WE NOW?
We’ve so far talked about a bunch of different blocking techniques
  Packet filtering/BGP manipulation
  Injecting RSTs
  Injecting DNS replies
Those can all be used to block HTTP (and other types of content)
Our focus now: proxies and blocking mechanisms that act specifically on HTTP traffic.

## Slide 50: In-path censorship
Rather than sitting as a wiretap, actually intercept all traffic
  Now the censor can remove undesired packets
Two possible mechanisms:
  Flow Terminating
  Flow Rewriting
Two possible targets:
  Partial Proxying
  Complete Proxying

## Slide 51: Flow Terminating proxies

## Slide 52: Flow terminating
Proxy
External Server
SYN
SYN
SYNACK
SYNACK
ACK
ACK
Two separate TCP connections.
Buys the censor some time to process content.
No worry about having to match state because the proxy is the end point (from client’s point of view)
External Server might see client IP, might see Proxy IP

## Slide 53: Flow rewriting proxies

## Slide 54: Flow Rewriting
Proxy
External Server
SYN
SYN
SYNACK
SYNACK
ACK
ACK

## Slide 55: Flow Rewriting
Proxy
External Server
Censored keyword
Block Page

## Slide 56: Partial vs. complete proxying

## Slide 57: Detecting and using partial proxies

## Slide 58: Detecting complete terminating proxies

## Slide 59: Overview
Block IP addresses
  IP layer
Disrupt TCP flows
  TCP (transport layer)
  Many possible triggers
Block hostnames
  DNS (application layer)
Disrupt HTTP transfers
  HTTP (application layer)
Fingerprinting filtering products

## Slide 60: Trend: New economic models of attacks
Traditional spam: Financially-motivated adversaries targeting many users
$
Notes: A trend with this sort of malware is that it changes the way we think about the economics of spam and security.
You can imagine your flight by night spammer ….

## Slide 61: Trend: New economic models of attacks
Traditional spam: Financially-motivated adversaries targeting many users
Targeted threats: Politically-motivated actors honing in on specific targets
$
information

## Slide 62: Huge market for censorship/surveillance products
Estimated sales of $5 billion per year for surveillance/wiretapping products*
Products developed by Western countries!
*http://www.washingtonpost.com/world/national-security/trade-in-surveillance-technology-raises-worries/2011/11/22/gIQAFFZOGO_story.html

## Slide 63: Filtering products…
Dual use technology …
  Keep employees off Facebook, keep schoolchildren safe from inappropriate content
…but in the wrong hands
  Human rights violations
  Surveillance
  Censorship
  …

## Slide 69: This has not gone unnoticed…
http://www.bloomberg.com/news/2012-04-23/obama-moves-to-block-technology-used-by-regimes-against-protests.html
Notes: This fact has not gone unnoticed with the EU, US and Israel all putting sanctions in place to limit the export of these products.
============
The fact that we are shipping products for cnsorship and surveillance around the world hasn’t gone unnoticed. The US, Europe and Israel have all implemented various sanctions against export of these products to foreign governments.

## Slide 71: How to enforce restrictions?
… and monitor emerging issues …
Need techniques to identify installations of these products in regions around the world
AND confirm that they are used for censorship

## Slide 72: Step 1: find suspected installations
Observe the logo of the product on a block page…
  … getting more challenging as products work to conceal themselves
Look for user reports of the product being used
  …incomplete, requires technically savvy users (see previous bullet)
Scans of publicly accessible IP address space
  …requires that the product be configured with a globally routable IP address
  Best we have right now …

## Slide 73: Examples of user reports

## Slide 74: Sources of Scan data
Shodan
Internet Census (ethics?)

## Slide 75: Ok … but what to scan for?
Signatures/strings to look for derived from hands on testing/observations of censorship

## Slide 79: Netsweeper

## Slide 80: Netsweeper

## Slide 81: Netsweeper

## Slide 82: Netsweeper

## Slide 83: netsweeper

## Slide 84: Terms to search for (Shodan)

## Slide 85
Need to confirm that these IPs are actually still hosting the product

## Slide 88: Where we found installations

## Slide 89: OK … so we’ve found an installation
Is it being used for censorship?
Can be easy ….

## Slide 90: Or not …

## Slide 91: How to confirm censorship
… even if the logo is not on the block page
  Leverage the fact that URLs are a key piece of the censorship product’s features

## Slide 92: Identifying Commercial Filtering Devices
Create 10 proxy Web sites (have these domains host a simple proxy script, Glype)
Check that these sites are not blocked (shouldn’t be since they are created just for this purpose).
http://bargaindeputy.com
http://zipzoodle.com
http://thatsit.com
http://steamrafts.com
http://notabigdeal.com
http://electroacoustic.com
http://whatandthehow.com
http://elasticmanniquin.com
http://swimstartz.com
http://evadingape.com

## Slide 93: Identifying Commercial Filtering Devices
Take 5 domains
http://bargaindeputy.com
http://zipzoodle.com
http://thatsit.com
http://steamrafts.com
http://notabigdeal.com
http://electroacoustic.com
http://whatandthehow.com
http://elasticmanniquin.com
http://swimstartz.com
http://evadingape.com

## Slide 94: Identifying Commercial Filtering Devices
And submit them for classification on the suspected device categorization page.
http://bargaindeputy.com
http://zipzoodle.com
http://thatsit.com
http://steamrafts.com
http://notabigdeal.com
http://electroacoustic.com
http://whatandthehow.com
http://elasticmanniquin.com
http://swimstartz.com
http://evadingape.com

## Slide 95: Identifying Commercial Filtering Devices
http://bargaindeputy.com
http://zipzoodle.com
http://thatsit.com
http://steamrafts.com
http://notabigdeal.com
http://electroacoustic.com
http://whatandthehow.com
http://elasticmanniquin.com
http://swimstartz.com
http://evadingape.com
Submitted Sample
Control Group

## Slide 96: Identifying Commercial Filtering Devices
Check again in Country X if they are blocked
http://bargaindeputy.com
http://zipzoodle.com
http://thatsit.com
http://steamrafts.com
http://notabigdeal.com
http://electroacoustic.com
http://whatandthehow.com
http://elasticmanniquin.com
http://swimstartz.com
http://evadingape.com
Submitted Sample
Control Group

## Slide 97: Results

## Slide 98: What are these products censoring?
Many of these categories of speech protected under UN declaration of human rights

## Slide 99: Other approaches to fingerprinting
Challenge of site submission is that it relies on the site submission interface existing for a product.
…Also need the product to be globally routable to find it’s IP address.
Other approaches
  Look for HTTP header changes (hit your own server see what the headers are passed on as)
    CoNteNT LeNGth -> content length
  HTML structure of block pages
    Common templates for the same product.
    Easy to identify via html tag frequencies

## Slide 100: HTML block page fingerprinting
HTML structure of block pages
  Common templates for the same product.
  Easy to identify via html tag frequencies
  Sometimes mapping to product is tricky
  Enables historical analysis

## Slide 101: Hands on activities
Some interactive activities you can try 

## Slide 102: Hands on activity
http://netalyzr.icsi.berkeley.edu/restore/id=43ca208a-16353-81bcc662-d580-4088-824f
http://netalyzr.icsi.berkeley.edu/restore/id=36ea240d-13470-a97f9d6d-ef09-4b43-b19b
Where were these Netalyzr tests run?
Do they seem to use the same censorship product?
What can you learn about these connections from Netalyzr?

## Slide 103: Hands on activity
Look up a filtering product in Shodan
  (will need to make a free account if you want to search in a specific country)
Download/run WhatWeb on the IP you find
  Is it still running the product?
What network is it in?
Check out the Internet census data
  Anything interesting there?
http://internetcensus2012.bitbucket.org/paper.html