## Slide 1: CSE390 – Advanced Computer Networks
Lecture 16: Data center networks
(The Underbelly of the Internet)
Based on slides by D. Choffnes @ NEU. Updated by P. Gill Fall 2014.

## Slide 2: “The Network is the Computer”
Network computing has been around forever
  Grid computing
  High-performance computing
  Clusters
Highly specialized
  Nuclear simulation
  Stock trading
  Weather prediction
All of a sudden, datacenters/the cloud are HOT
  Why?

## Slide 3: The Internet Made Me Do It
Everyone wants to operate at Internet scale
  Millions of users
    Can your website survive a flash mob?
  Zetabytes of data to analyze
    Webserver logs
    Advertisement clicks
    Social networks, blogs, Twitter, video…
Not everyone has the expertise to build a cluster
  The Internet is the symptom and the cure
  Let someone else do it for you!

## Slide 4: The Nebulous Cloud
What is “the cloud”?
Everything as a service
  Hardware
  Storage
  Platform
  Software
Anyone can rent computing resources
  Cheaply
  At large scale
  On demand

## Slide 5: Example: Amazon EC2
Amazon’s Elastic Compute Cloud
  Rent any number of virtual machines
  For as long as you want
Hardware and storage as a service

## Slide 6: Example: Google App Engine
Platform for deploying applications
From the developers perspective:
  Write an application
  Use Google’s Java/Python APIs
  Deploy app to App Engine
From Google’s perspective:
  Manage a datacenter full of machines and storage
  All machines execute the App Engine runtime
  Deploy apps from customers
  Load balance incoming requests
  Scale up customer apps as needed
    Execute multiple instances of the app

## Slide 10: Data center networks overview
Internet
Servers
Top of Rack (ToR) switch
Aggregation “Agg” switch
Load balancers
Access routers/network “core” fabric
Notes: Before looking at properties of failures lets first take a step back and look at the architecture of the data center network ...
This slide shows an example of a data center network architecture. It is a hierarchical structure with servers at the bottom of the topology. Servers connect to Top of Rack or ToR switches which in turn connect to a redundant set of aggregation switches. Each aggregation switch connects to a set of load balancers that are used to distribute traffic across servers. The Aggregation switches then connect to access and core routers that provide connectivity to the Internet.

## Slide 11: Advantages of Current Designs
Cheap, off the shelf, commodity parts
  No need for custom servers or networking kit
  (Sort of) easy to scale horizontally
Runs standard software
  No need for “clusters” or “grid” OSs
  Stock networking protocols
Ideal for VMs
  Highly redundant
  Homogeneous

## Slide 12: Lots of Problems
Datacenters mix customers and applications
  Heterogeneous, unpredictable traffic patterns
  Competition over resources
  How to achieve high-reliability?
  Privacy
Heat and Power
  30 billion watts per year, worldwide
  May cost more than the machines
  Not environmentally friendly
All actively being researched

## Slide 13: Today’s Topic : Network Problems
Datacenters are data intensive
Most hardware can handle this
  CPUs scale with Moore’s Law
  RAM is fast and cheap
  RAID and SSDs are pretty fast
Current networks cannot handle it
  Slow, not keeping pace over time
  Expensive
  Wiring is a nightmare
  Hard to manage
  Non-optimal protocols

## Slide 14: Outline
Intro
Network Topology and Routing
Transport Protocols
  Google and Facebook
  DCTCP
  D3
Reliability

## Slide 15: Problem: Oversubscription
40 Machines
1 Gbps Each
1:4
40x1 Gbps Ports
40x1Gbps  1x10 Gbps
1:80-240
#Racksx40x1 Gbps  1x10 Gbps
1:1
Bandwidth gets scarce as you move up the tree
Locality is key to performance
All-to-all communication is a very bad idea
Notes: Port bundling

## Slide 16: Consequences of Oversubscription
Oversubscription cripples your datacenter
  Limits application scalability
  Bounds the size of your network
Problem is about to get worse
  10 GigE servers are becoming more affordable
  128 port 10 GigE routers are not
Oversubscription is a core router issue
  Bottlenecking racks of GigE into 10 GigE links
What if we get rid of the core routers?
  Only use cheap switches
  Maintain 1:1 oversubscription ratio

## Slide 17: Fat Tree Topology
To build a K-ary fat tree
K-port switches
K3/4 servers
(K/2)2 core switches
K pods, each with K switches
In this example K=4
4-port switches
K3/4 = 16 servers
(K/2)2 = 4 core switches
4 pods, each with 4 switches
Pod

## Slide 18: Fat Tree at a Glance
The good
  Full bisection bandwidth
  Lots of redundancy for failover
The bad
  Need custom routing
    Paper uses NetFPGA
  Cost  3K2/2 switches
    48 port switches = 3456 switch
The ugly
  OMG TEH WIRES!!!!  (K3+2K2)/4
    48 port switches = 28800

## Slide 19: Is Oversubscription so Bad?
Oversubscription is a worst-case scenario
  If traffic is localized, or short, there is no problem
How bad is the problem?

## Slide 20: Idea: Flyways
Challenges
  Additional wiring
  Route switching
Paper: http://research.microsoft.com/pubs/157700/flyways_sigcomm11.pdf

## Slide 21: Wireless Flyways
Why use wires at all?
Connect ToR servers wirelessly
Why can’t we use Wifi?
  Massive interference
Key issue: Wifi is not directed

## Slide 22: Direction 60 GHz Wireless

## Slide 23: Implementing 60 GHz Flyways
Pre-compute routes
  Measure the point-to-point bandwidth/interference
  Calculate antenna angles
Measure traffic
  Instrument the network stack per host
  Leverage existing schedulers
Reroute
  Encapsulate (tunnel) packets via the flyway
  No need to modify static routes

## Slide 24: Results for 60 GHz Flyways
Hotspot fan-out is low
You don’t need that many antennas per rack
Adding a 2nd antenna 40% of flows complete as fast as non-oversubscribed network.
Prediction/scheduling is super important
Better schedulers could show more improvement
Traffic aware schedulers?
CTD = time for last flow to complete (completion time of the demands)
Which traffic to put on the flyway?
How many antennas per rack?

## Slide 25: Problems with Wireless Flyways
Problems
  Directed antennas still cause directed interference
  Objects may block the point-to-point signal

## Slide 26: 3D Wireless Flyways
Prior work assumes 2D wireless topology
  Reduce interference by using 3D beams
  Bounce the signal off the ceiling!
Stainless Steel Mirrors
60 GHz Directional Wireless

## Slide 27: Comparing Interference
2D beam expands as it travels
  Creates a cone of interference
3D beam focuses into a parabola
  Short distances = small footprint
  Long distances = longer footprint

## Slide 28: Scheduling Wireless Flyways
Problem: connections are point-to-point
  Antennas must be mechanically angled to form connection
  Each rack can only talk to one other rack at a time
How to schedule the links?
Proposed solution
  Centralized scheduler that monitors traffic
  Based on demand (i.e. hotspots), choose links that:
    Minimizes interference
    Minimizes antenna rotations (i.e. prefer smaller angles)
    Maximizes throughput (i.e. prefer heavily loaded links)
NP-Hard scheduling problem
Greedy algorithm for approximate solution

## Slide 29: Other issues
Ceiling height
Antenna targeting errors
Antenna rotational delay

## Slide 30: Modular Datacenters
Shipping container “datacenter in a box”
  1,204 hosts per container
  However many containers you want
How do you connect the containers?
  Oversubscription, power, heat…
  Physical distance matters (10 GigE  10 meters)

## Slide 31
MSFT’s Chicago DC is containers!

## Slide 32: Possible Solution: Optical Networks
Idea: connect containers using optical networks
  Distance is irrelevant
  Extremely high bandwidth
Optical routers are expensive
  Each port needs a transceiver (light  packet)
  Cost per port: $10 for 10 GigE, $200 for optical

## Slide 33: Helios: Datacenters at Light Speed
Idea: use optical circuit switches, not routers
  Uses mirrors to bounce light from port to port
  No decoding!
Tradeoffs
  Router can forward from any port to any other port
  Switch is point to point
  Mirror must be mechanically angled to make connection
In Port
Out Port
Mirror
In Port
Out Port
Transceiver
Transceiver
Optical
Router
Optical
Switch
http://cseweb.ucsd.edu/~vahdat/papers/helios-sigcomm10.pdf

## Slide 34: Dual Optical Networks
Typical, packet switch network
  Connects all containers
  Oversubscribed
  Optical routers
Fiber optic flyway
  Optical circuit switch
  Direct container-to-container links, on demand

## Slide 35: Circuit Scheduling and Performance
Centralized topology manager
  Receives traffic measurements from containers
  Analyzes traffic matrix
  Reconfigures circuit switch
  Notifies in-container routers to change routes
Circuit switching speed
  ~100ms for analysis
  ~200ms to move the mirrors

## Slide 36: Outline
Intro
Network Topology and Routing
Transport Protocols
  Google and Facebook
  DCTCP
Reliability

## Slide 37: Transport on the Internet
TCP is optimized for the WAN
  Fairness
    Slow-start
    AIMD convergence
  Defense against network failures
    Three-way handshake
    Reordering
  Zero knowledge congestion control
    Self-induces congestion
    Loss always equals congestion
  Delay tolerance
    Ethernet, fiber, Wi-Fi, cellular, satellite, etc.

## Slide 38: Datacenter is not the Internet
The good:
  Possibility to make unilateral changes
    Homogeneous hardware/software
    Single administrative domain
  Low error rates
The bad:
  Latencies are very small (250µs)
    Agility is key!
  Little statistical multiplexing
    One long flow may dominate a path
    Cheap switches have queuing issues
  Incast

## Slide 39: Partition/Aggregate Pattern
Common pattern for web applications
  Search
  E-mail
Responses are under a deadline
  ~250ms
Web Server
Aggregators
Workers
User Request
Response

## Slide 40: Problem: Incast
Aggregator sends out queries to a rack of workers
  1 Aggregator
  39 Workers
Each query takes the same time to complete
All workers answer at the same time
  39 Flows 1 Port
  Limited switch memory
  Limited buffer at aggregator
Packet losses :(
Aggregator
Workers

## Slide 41: Problem: Buffer Pressure
In theory, each port on a switch should have its own dedicated memory buffer
Cheap switches share buffer memory across ports
  The fat flow can congest
  the thin flow!

## Slide 42: Problem: Queue Buildup
Long TCP flows congest the network
  Ramp up, past slow start
  Don’t stop until they induce queuing + loss
  Oscillate around max utilization
Short flows can’t compete
  Never get out of slow start
  Deadline sensitive!
  But there is queuing on arrival

## Slide 43: Industry Solutions Hacks
  Limits search worker responses to one TCP packet
  Uses heavy compression to maximize data
  Largest memcached instance on the planet
  Custom engineered to use UDP
  Connectionless responses
  Connection pooling, one packet queries

## Slide 44: Dirty Slate Approach: DCTCP
Goals
  Alter TCP to achieve low latency, no queue buildup
  Work with shallow buffered switches
  Do not modify applications, switches, or routers
Idea
  Scale window in proportion to congestion
  Use existing ECN functionality
  Turn single-bit scheme into multi-bit

## Slide 45: Explicit Congestion Notification
Use TCP/IP headers to send ECN signals
  Router sets ECN bit in header if there is congestion
  Host TCP treats ECN marked packets the same as packet drops (i.e. congestion signal)
    But no packets are dropped :)
No Congestion
Congestion
ECN-bit set in ACK
Sender receives feedback

## Slide 46: ECN and ECN++
Problem with ECN: feedback is binary
  No concept of proportionality
  Things are either fine, or disasterous
DCTCP scheme
  Receiver echoes the actual EC bits
  Sender estimates congestion (0 ≤ α ≤ 1) each RTT based on fraction of marked packets
  cwnd = cwnd * (1 – α/2)

## Slide 47: DCTCP vs. TCP+RED

## Slide 48: Flow/Query Completion Times

## Slide 49: Shortcomings of DCTCP
Benefits of DCTCP
  Better performance than TCP
  Alleviates losses due to buffer pressure
  Actually deployable
But…
  No scheduling, cannot solve incast
  Competition between mice and elephants
  Queries may still miss deadlines
Network throughput is not the right metric
  Application goodput is
  Flows don’t help if they miss the deadline
  Zombie flows actually hurt performance!

## Slide 50: Outline
Intro
Network Topology and Routing
Transport Protocols
  Google and Facebook
  DCTCP
Reliability

## Slide 51: Motivation
$5,600 per minute
We need to understand failures to prevent and mitigate them!
Notes: As we have seen in many high profile incidents reliability of data center networks is crucial to service availability. For example, Amazon experienced a high profile outage this past April when upgrading a network link. This outage had severe impact on numerous popular online services. These outages that impact numerous services hosted in the same data centers have high cost to organizations hosting them. For example this study finds that on average unplanned outages cost $5600 per minute.
The overarching goal of our research is to improve the reliability of services hosted in data centers by getting a better understanding of causes and properties of failure events.
=======
When failures occur in cloud computing systems they make big news. In particular, you are probably familiar with the Amazon EC2 outage that happened in April 2011. This incident made major news not only because Amazon failed but because this failure impacted many sites that were hosted on Amazon. [http://ec2disabled.com/] such as Reddit and Hootsuite a social media site.
In addition to noticeable customer outages in cloud computing can be extremely costly [http://www.informationweek.com/news/hardware/data_centers/229500121]. One study finds that data center outages can cost $5600/minute on average and an average outage duration of 90 minutes leads to an average of half a million dollars per incident. The survey reported on in this article also finds that 95% of organizations surveyed had at least 1 unplanned outage.
Networking can play a role in these outages and in fact a network upgrade combined with configuration error that caused traffic to flow along a lower capacity secondary link.
In this study we shed light on network faults to enable the development strategies for mitigating their impact.
Amazon outage, since many services share a common substrate in cloud computing when there is an outage many services are impacted
As a result these outages are extremely expensive average of half a million per incident
Networking has a role to play in terms of preventing outages (e.g., Amazon outage was a configuration error when upgrading network capacity. We need tools to prevent configuration errors and better mitigate failures once they have happened!)
A common pattern across these outages is that network gets the blame’ which motivates this work of understanding network reliability in DCs
------
From: http://aws.amazon.com/message/65648/
At 12:47 AM PDT on April 21st, a network change was performed as part of our normal AWS scaling activities in a single Availability Zone in the US East Region. The configuration change was to upgrade the capacity of the primary network. During the change, one of the standard steps is to shift traffic off of one of the redundant routers in the primary EBS network to allow the upgrade to happen. The traffic shift was executed incorrectly and rather than routing the traffic to the other router on the primary network, the traffic was routed onto the lower capacity redundant EBS network.
For a portion of the EBS cluster in the affected Availability Zone, this meant that they did not have a functioning primary or secondary network because traffic was purposely shifted away from the primary network and the secondary network couldn’t handle the traffic level it was receiving.
-----
What is meant by cost: Utilizing activity-based costing, our methods capture information about both direct and indirect
costs, including but not limited to the following areas:
 Damage to mission critical data
 Impact of downtime on organizational productivity
 Damages to equipment and other assets
 Cost to detect and remediate systems and core business processes
 Legal and regulatory impact, including litigation defense cost
 Lost confidence and trust among key stakeholders
 Diminishment of marketplace brand and reputation

## Slide 52: Overview
Our goal: Improve reliability by understanding network failures
Failure characterization
  Most failure prone components
  Understanding root cause
What is the impact of failure?
Is redundancy effective?
Our contribution: First large-scale empirical study of network failures across multiple DCs
Methodology to extract failures from noisy data sources.
Correlate events with network traffic to estimate impact
Analyzing implications for future data center networks
Notes: ….towards this goal we take the initial step of understanding the properties of network failures in a data center network. We consider the properties of network failures along 3 dimensions
-What are the properties of failures. Which components are most failure prone, what causes failure and how long does failure take to resolve.
-we also consider the impact of failures on network traffic and
-how effective network level redundancy is at masking impact.
Our main contribution here is the first large scale empirical study of failures in a data center network comprised of multiple data centers hosting numerous popular online services.
-part of our contribution comes in the form of methodology to extract and reconstruct failures in our very rich, but sometimes noisy data set.
-further we correlate the network failures with network traffic to understand impact
-and finally we consider implications of our findings for future data center network architectures.
===
-> which components are most failure prone? Is there a specific part of the network where attention should be focused to maximize reliability?
-> what are the main causes of failure? Is it a software issue that may be remedied by writing better code or are failures caused by intrinsic hardware problems?
We want to determine the impact of failures. Many failure alerts may be present in the system but we want to understand how much impact they have on network traffic? How do these impacts potentially impact traffic flows?
-> Finally data center networks are built to have redundant components so we look at how effective this redundancy is in terms of mitigating failure impact. As we see in the Amazon case, sometimes configuration errors can render redundancy ineffective.
To meet this goal we perform the first large scale study of network failures in data centers.
We do this by analyzing logged failure events in a production data center network comprised of multiple data centers.
Due to the scale of the network the volume of messages logged by the various components was extremely large so we needed to develop a methodology to extract failures with impact from the set of all logs. We also correlate between failure logs and network traffic to get a better understanding of how failures we consider impact network traffic.
Finally, we draw implications of our results for future data center network designs.

## Slide 53: Data center networks overview
Internet
How effective is redundancy?
What is the impact of failure?
Which components are most failure prone?
What causes failures?
?
Notes: Using this topology as a guide we can think about what questions we would like to answer about data center network reliability.
First we want to understand which components are most failure prone. For example, are certain parts of the topology more impacted by failures and are their components we can focus on to mitigate most of the failures.
Next we want to understand what are the causes of failures. Are they software problems where redesigning software will help or intrinsic hardware problems that need to be designed around.
We also want to know what the impact of network failures is on network flows in the data center.
Finally, since we have redundant sets of components in our network we want to see how effective they are in masking failure events.

## Slide 54: Failure event information flow
Failure is logged in numerous data sources
LINK DOWN!
Syslog, SNMP traps/polling
Network event logs
Troubleshooting
Tickets
Troubleshooting
LINK DOWN!
Ticket ID: 34
LINK DOWN!
Diary entries,
root cause
Network traffic logs
5 min traffic averages on links
Notes: Before we can try to answer these questions with our data we need to understand how failures are logged. In our network failures are logged by multiple sources. For example if we have a link between two devices that fails it will be logged in network event logs which detect the failure via Syslog, SNMP traps and polling. The network event logging system will also automatically generate a trouble shooting ticket associated with the event.
Before we try to analyze failure events in our network its important to understand the logging infrastructure that tracks failure events.
… talk through logging components.
We also have access to network traffic logs that we can correlate with the network event logs to understand the impact of logged events.
Challenges:
High volume -> needed a precise definition of failure for our study in order to reduce volume.
Noisy data sources -> needed to reconstruct link and device state using heuristics
Correlating failures with additional data -> Correlate with traffic averages to determine impact.

## Slide 55: Data summary
One year of event logs from Oct. 2009-Sept. 2010
  Network event logs and troubleshooting tickets
Network event logs are a combination of Syslog, SNMP traps and polling
  Caveat: may miss some events e.g., UDP, correlated faults
Filtered by operators to actionable events
  … still many warnings from various software daemons running
Key challenge: How to extract failures of interest?
Notes: Our main source of data in this study is the network event logs. These are 1 year of events from Oct. 2009 until Oct. 2010 in the data centers that make up our network. Each failure event contains information on the component that failed, for example if it was a link, switch, or router. It also contains information about the severity of the event, whether it is a warning or more serious incident. It also contains a small textual description of the event as well as the time at which the event was resolved.
The logs are generated using data from SNMP polling and traps as well as syslog messages. Since all of this logging is best effort it may be the case that occasionally messages are lost (for example because of UDP messages being lost).
The logs are also filtered by the administrators to remove some spurious messages. For example, Syslog link down messages are ignored because they tend to occur on port flapping which does not impact connectivity. However, there was still a large number of events that were not necessarily severe. For example, warnings logged by software daemons running on load balancers.
We took a bottom up approach in terms of extracting events of interest from these logs by extracting events relating to device and link failures.

## Slide 56: Extracting failures from event logs
Network event logs
Defining failures
  Device failure: device is no longer forwarding traffic.
  Link failure: connection between two interfaces is down. Detected by monitoring interface state.
Dealing with inconsistent data:
  Devices:
    Correlate with link failures
  Links:
    Reconstruct state from logged messages
    Correlate with network traffic to determine impact
Notes: To extract device and link failures we first had to define what is meant by failure. For devices these were messages where switches, routers or load balancers reported that they were “down”. In this case “down” does not necessarily mean the device is replaced but that it is not functioning for forwarding traffic. So a device that repeatedly power cycles will manifest as multiple device failure events.
Link failures on the otherhand indicate that the connection between two devices on specific interfaces is down. This is measured by monitoring the interface state on devices and raising an alert if the state is no longer connected.
Even with these more precise definitions of failure we still had an extremely large number of events. So we used some sanity tests to reconstruct state for the links and devices to rule out spurious notifications. For link failures we were also able to correlate failures with network traffic and identify failure events where the event impacted network traffic.

## Slide 57: Identifying failures with impact
Summary of impact:
  28.6% of failures impact network traffic
  41.2% of failures were on links carrying no traffic
    E.g., scheduled maintenance activities
Caveat: Impact is only on network traffic not necessarily applications!
  Redundancy: Network, compute, storage mask outages
Network traffic logs
LINK DOWN
LINK UP
BEFORE
DURING
AFTER
Correlate link failures with network traffic
time
Only consider events where traffic decreases
Notes: Once we have reconstructed the states for all the link failures we observe we then correlate these failure events with network traffic to verify that the failures we observe in the logs indeed impact network traffic. So how we do this is we have the time of the link down and link up messages. We then look at network logs and observe the traffic on the link before and during the failure. We say that a failure had impact if traffic on the link experiencing the failure decreases during the failure. We only require that traffic decrease because our traffic logs were in 5 minute bins and the majority of failures lasted less than 5 minutes. So the link may have been up for a portion of the 5 minute interval.
The effect of ruling out failures where traffic did not decrease during failure was that only 28% of our failures impact network traffic and that 41% of the failures happened on links that were not carrying traffic at the time. These are likely maintenance events.
One thing to bear in mind here is that when we talk about impact we’re looking at impact in terms of network traffic and not necessarily applications. So our notion of failure or availability here should not be interpreted as being application outages.
Correlate link failures with network traffic
Only consider failures where network traffic decreased
  5 minute traffic averages mean traffic will not always be zero

## Slide 58: Visualization of failure panorama: Sep’09 to Sep’10
All Failures 46K
Chart: Time (binned by day)
Chart: Time (binned by day)
Failures with Impact 28%
Load balancer update
(multiple data centers)
Component failure: link failures on multiple ports
Widespread failures
Long lived failures.
Link Y had failure on day X.
Notes: We can now take a global view of link failures in our network. This figure shows at a high level view the distribution of failures across space and time …
See impact of only considering failures with impact
Observe if there are widespread or long lived failures

## Slide 59: Which devices cause most failures?
Internet
Notes: We next look more in detail at where in the network failures occur by considering which components are most failure prone. The goal here is to understand if there is specific part of the network that we can prioritize in order to improve reliability the most.

## Slide 60: Which devices cause most failures?
Chart: Device type
| f6f | f6x | 49x | f8x | 30x | 65ag
failures | 0.37795 | 0.28493 | 0.15488 | 0.094697 | 0.044192 | 0.04335
downtime | 0.018561 | 0.18319 | 0.66286 | 0.054243 | 0.076904 | 0.0042439
Top of rack switches have few failures…
(annual prob. of failure <5%)
Load balancer 1: very little downtime relative to number of failures.
…but a lot of downtime!
Load
Balancer 1
Load
Balancer 2
Top of
Rack 2
Aggregation
Switch
Top of
Rack 1
Load
Balancer 3
Device Type
Notes: We first look at which devices fail the most.
This graph shows the fraction of failures and downtime attributed to each device type
We see that load balancer 1 has the most failures, but very little down time
This is opposite to what we see for top of rack switches where there is very few failures. ToRs have the lowest probability of failure of any device with ToRs having failure rates of less than 5% (more detail on probability of failure is in the paper).
… but the highest amount of downtime. This is because ToRs are not a high priority component for repairs because of application level redundancy of compute and storage.

## Slide 61: How long do failures take to resolve?
Internet

## Slide 62: How long do failures take to resolve?
Load balancer 1: short-lived transient faults
Correlated failures on ToRs connected to the same Aggs.
Median time to repair:
4 mins
Median time to repair:
ToR-1: 3.6 hrs
ToR-2: 22 min
Median time to repair: 5 minutes
Mean: 2.7 hours
Load Balancer 1
Load Balancer 2
Top of Rack 1
Load Balancer 3
Top of Rack 2
Aggregation Switch
Overall
Notes: We now take a look at the properties of the failures of these devices.
This plot shows the CDF of time to repair (ie., time between when a failure starts and ends) for the different devices
Here we can see the cause of ToRs having high downtime. Steps = correlated downtime of ToRs connecting to the same Agg.
When we look at failures for load balancer 1 we can see that many of them are short lived with most being resolved in 5 minutes (so mostly self healing software issues).

## Slide 63: Summary
Data center networks are highly reliable
  Majority of components have four 9’s of reliability
Low-cost top of rack switches have highest reliability
  <5% probability of failure
…but most downtime
  Because they are lower priority component
Load balancers experience many short lived faults
  Root cause: software bugs, configuration errors and hardware faults
Software and hardware faults dominate failures
  …but hardware faults contribute most downtime
Notes: stress on criticality of control plane/middleboxes/LBs in DC network ops -- not just high bisection bandwidth.
Low cost switches are reliable-> good for proposals leveraging commodity components
Load balancers have software issues -> more thought needs to go into how middle boxes are managed in data centers.

## Slide 64: Is redundancy effective in reducing impact?
Internet
Redundant devices/links to mask failures
This is expensive! (management overhead + $$$)
Goal: Reroute traffic along available paths
How effective is this in practice?
X

## Slide 65: Measuring the effectiveness of redundancy
Idea: compare traffic before and during failure
Measure traffic on links:
Before failure
During failure
Compute “normalized traffic” ratio:
  Compare normalized traffic over redundancy groups to normalized traffic on the link that failed
Agg.
switch
(primary)
Agg.
switch
(backup)
Acc. router
(primary)
Acc. router
(backup)
X

## Slide 66: Is redundancy effective in reducing impact?
Chart: Normalized traffic during failure (median)
| All | Top of Rack to Aggregation switch | Aggregation switch to Access router | Core
Per link | 0.65 | 0.68 | 0.42 | 0.27
Per redundancy group | 0.93 | 0.94 | 0.86 | 1
Core link failures have most impact…
… but redundancy masks it
Less impact lower in the topology
Redundancy is least effective for AggS and AccR
Overall increase of 40% in terms of traffic due to redundancy
Internet
Notes: We observe that redundancy isn’t completely effective in terms of mitigating failures.

## Slide 67: Outline
Intro
Network Topology and Routing
Transport Protocols
  Google and Facebook
  DCTCP
  D3
Reliability

## Slide 68: Big Open Problem
Measurement data
  Real datacenter traces are very hard to get
  Are they representative?
    Really, what is a ‘canonical’ datacenter?
    Application dependent
Makes results very hard to quantify
  Cross-paper comparisons
  Reproducibility