## Slide 1: CSE390 Advanced Computer Networks
Lecture 12-13: Internet Connectivity + IXPs
(The Underbelly of the Internet)
Based on slides by D. Choffnes (NEU), C. Labovitz, A. Feldmann, revised by P. Gill Fall 2014.

## Slide 2: Outline
Internet Connectivity
  The shift from hierarchy to flat
  Measuring the shift
IXPs

## Slide 3: The Internet as a Natural System
You’ve learned about the TCP/IP Internet
  Simple abstraction: Unreliable datagram transmission
  Various layers
  Ancillary services (DNS)
  Extra in-network support
So what is the Internet actually being used for?
  Emergent properties impossible to predict from protocols
  Requires measuring the network
  Constant evolution makes it a moving target

## Slide 4: Measuring the capital-I Internet*
Measuring the Internet is hard
Significant previous work on
  Router and AS-level topologies
  Individual link / ISP traffic studies
  Synthetic traffic demands
But limited “ground-truth” on inter-domain traffic
  Most commercial arrangements under NDA
  Significant lack of uniform instrumentation
*Mainly borrowed stolen from Labovitz 2010

## Slide 5: Conventional Wisdom (i.e., lies)
Internet is a global scale end-to-end network
  Packets transit (mostly) unmodified
  Value of network is global addressability /reachability
Broad distribution of traffic sources / sinks
An Internet “core” exists
  Dominated by a dozen global transit providers (tier 1)
  Interconnecting content, consumer and regional providers

## Slide 6: Does this still hold?
Emergence of ‘hyper giant’ services
How much traffic do these services contribute?
Hard to answer!
  Reading on Web page: Labovitz 2010 tries to look at this.

## Slide 7: Methodology
Focus on inter-domain traffic
Leverage widely deployed commercial Internet monitoring infrastructure
  Add export of coarse grain traffic statistics (ASNs, AS Paths, protocols, ports, etc)
Cajole carriers into participation
  110+ ISPs/content providers
  Including 3,000 edge routers and 100,000 interfaces
  Estimated 25% of all inter-domain traffic
Wait two years…

## Slide 8: Change in Carrier Traffic Demands
In 2007 top ten match “Tier 1” ISPs
In 2009 global transit carry significant volumes
  But Google and Comcast join the list
  Significant fraction of ISP A traffic is Google transit

## Slide 9: Consolidation of Content
In 2007 1,000s of ASes contribute 50% of traffic
In 2009, 150 ASes contribute 50% of traffic!

## Slide 10: Case Study: Google
Over time Google begins delivering YT’s traffic
As of 2009 Google is 6% of traffic

## Slide 11: Case Study: Comcast
2007 Comcast looks like ‘eyeball’ provider (more traffic in than out)
2009 this shifts. They look more like transit/content
Wholesale transit, video distribution etc.

## Slide 12: Market forces at play

## Slide 13: Market intuition
Commoditization of IP and hosting/CDN
  Drop in price of transit
  Drop in price of video/CDN
  Economics of scale  Cloud computing
Consolidation
  Big get bigger (economics of scale)
  Acquisitions (e.g., Google + YT)
New economic models
  Paid peering, paid content
Disintermediation
  Direct connections between content + consumer
  Cost + performance considerations

## Slide 14: New applications + ways to access them
Fixed vs. Mobile Usage

## Slide 15: The shift from hierarchy to flat
Local Access
Provider
Regional Access
Provider
AT&T
Sprint
Verizon
Regional Access
Provider
Tier 1 ISPs
(settlement free peering)
Tier 2 ISPs
Tier 3 ISPs
Local Access
Provider
Businesses/consumers
$
$
$
$
$
$
$$$
$
Money follows the arrows.
Autonomous systems (ASes) connect to each other based on business relationships.

## Slide 16: The shift from hierarchy to flat
Local Access
Provider
Regional Access
Provider
AT&T
Sprint
Verizon
Regional Access
Provider
Tier 1 ISPs
(settlement free peering)
Tier 2 ISPs
Tier 3 ISPs
Local Access
Provider
Businesses/consumers
$
IXP
$
$
Content provider no longer needs to pay for transit!
More “eyeballs” less $$
Local Access Provider doesn’t have to pay for consumer access to content!

## Slide 17: A new Internet model

## Slide 18: Outline
Internet Connectivity
  The shift from hierarchy to flat
  Measuring the shift
IXPs

## Slide 19: First saw this in 2008
traceroute to 74.125.229.18 (Google)
1 80.82.140.226 0.209 ms 0.129 ms 0.328 ms
2 80.82.140.42 0.539 ms 0.525 ms 0.498 ms
3 80.82.140.43 0.472 ms 0.451 ms 0.427 ms
4 195.66.226.125 1.066 ms 1.077 ms 1.075 ms
5 209.85.252.76 1.022 ms 0.943 ms 0.979 ms
6 216.239.43.192 76.558 ms 76.454 ms 75.900 ms
7 209.85.251.9 91.356 ms 93.749 ms 93.941 ms
8 64.233.175.34 92.907 ms 93.624 ms 94.090 ms
9 74.125.229.18 93.307 ms 93.389 ms 90.771 ms
LINX(UK)
Conjecture: Google is buying up dark fibre and building up a WAN to cut costs.

## Slide 20: We wondered how prevalent this was
Idea: Traceroute to large content providers see where the traceroute enters their network
  Optional reading: The Flattening Internet Topology: Natural Evolution, Unsightly Barnacles or Contrived Collapse? Gill et al. http://www3.cs.stonybrook.edu/~phillipa/papers/PAM08.pdf

## Slide 21: What we saw: Paths with no Tier 1s
60% of paths with no tier 1 ISP
(30 out of 50)

## Slide 22: Relative degree of top content providers
We saw many more neighboring ASes for the top content providers
(not just a few providers)
These numbers are actually way lower than the true degree of these ASes

## Slide 23: An initial map of connectivity
Google

## Slide 24: This study suggested something was happening…
…But didn’t exhaustively measure the phenomenon
Only traceroute data from a limited set of VPs
  50 paths to each domain
Observing and measuring flattening requires measurements of the entire Internet topology

## Slide 25: Measuring the Internet’s topology
What do we mean by topology?
  Internet as graph
  Edges? Nodes?
  Node = Autonomous System (AS); edge = connection.
Edges labeled with business relationship
Customer  Provider
Peer -- Peer
SBU
AT&T
Sprint

## Slide 26: So how do we measure this graph?
Passive approach: BGP route monitors
  Coverage of the topology
  Amount of visibility provided by each neighbor
Active approach: Traceroute
  From where?
  Traceroute gives series of IP addresses not ASes
Active approach: TransitPortal
  Much more control over what we see
  …scalability/coverage?

## Slide 27: Passive approach: BGP Route Monitors
Receive BGP announcements from participating ASes at multiple vantage points
www.routeviews.org
Regional ISP
“originally motivated by interest on the part of operators in determining how the global routing system viewed their prefixes and/or AS space”
www.routeviews.org

## Slide 28: Going from BGP Updates to a Topology
Example update:
TIME: 03/22/11 12:10:45
FROM: 12.0.1.63 AS7018
TO: 128.223.51.102 AS6447
ASPATH: 7018 4134 9318 32934 32934 32934
69.171.224.0/20
AT&T (AS7018) it telling
Routeviews (AS 6447) about this route.
This /20 prefix can be reached via the above path

## Slide 29: Going from BGP Updates to a Topology
Key idea
  The business relationships determine the routing policies
  The routing policies determine the paths that are chosen
  So, look at the chosen paths and infer the policies
Example: AS path “7018 4134 9318” implies
  AS 4134 allows AS 7018 to reach AS 9318
  China Telecom allows AT&T to reach Hanaro Telecom
  Each “triple” tells something about transit service

## Slide 30: Why are peering links hard to see?
The challenge:
  BGP announcements do not reflect complete connectivity information
  They are an agreement to transit traffic for the AS they are advertised to…
Local ISP
Regional ISP
Small
business
Local ISP, Google
$
Local ISP will only tell his customers about the peering link.
Local ISP, Small business
Neither will Routeviews
Regional ISP won’t see the peering edge!
(ASes only transit traffic if it generates revenue!)
  Combination of no valley routing policy and a lack of monitors in stub ASes mean missing up to 90% of peering links of content providers! (Oliveria et al. 2008)

## Slide 31: Active approach: Traceroute
Issue: Need control over end hosts to run traceroute
  How to get VPs?
http://www.traceroute.org/
  Collection of O(100) servers that will run traceroute
  Hosted by ISPs/other network operators (e.g. universities)
RIPE Atlas
  Distribute specialized hardware to volunteers
  O(1000s) of probes
Dasu
  Bittorrent plug in that does measurements
  O(200) ASes with Dasu clients

## Slide 32: Where the sidewalk ends (CoNEXT 2009) (1/2)
Idea: Leverage traceroutes from P2P clients to extend the AS graph
Local ISP1
Regional ISP
Local ISP2
$
Routeviews will not be able to see this peering link because of “valley free” routing.
Vuze clients running Ono* plug in (Dasu predecessor)
(992K IPs, 3,700 ASes)
*D. Choffnes and F. Bustamante. Taming the Torrent: A practical approach to reducing cross-ISP traffic in P2P systems, SIGCOMM 2008.
As part of Ono these clients randomly traceroute to other (nearby) peers.
Mock traceroute:
IP ISP 1 (client1)
…
IP ISP 1 (router)
IP ISP 2 (router)
…
IP ISP 2 (client2)
NB: going from traceroute to AS connectivity is non-trivial!

## Slide 33: Where the sidewalk ends (CoNEXT 2009) (2/2)
23,914 new AS links
13% more customer provider links
41% more peering links
Tier 1s
“stubs”

## Slide 34: Active Approach: Transit Portal
Motivation: Traceroute/BGP monitors will only show us paths that are in use…
  … not full connectivity
Need to explore back up paths to find all the full AS-level topology
Transit Portal solution:
  AS + Prefix controlled by researchers
  Border of the research AS made up by participating institutions
  BGPMux at each institution acts as border router, multiplexes TP users, sends BGP updates out.

## Slide 35: Transit Portal Coverage
(SBU coming soon!)

## Slide 36: Using TP to explore connectivity
Similar idea as LIFEGUARD …
B
C
D
A
Prefix
Traceroute VP
TP
Prefix
B, TP
Prefix
C, TP
Prefix
D, TP
Prefix
A, B, TP
Prefix
TP

## Slide 37: Using TP to explore connectivity
Similar idea as LIFEGUARD …
B
C
D
A
Prefix
Traceroute VP
TP, B, TP
Prefix
C, TP, B, TP
Prefix
D, TP, B, TP
Prefix
A, C, TP, B, TP
Prefix
TP

## Slide 38: Using TP to explore connectivity
Similar idea as LIFEGUARD …
B
C
D
A
Prefix
Traceroute VP
TP, B, C, TP
Prefix
D, TP, B, C, TP
Prefix
A, D, TP, B, C TP
Prefix
TP
This is a simplified view …
in reality AS prepending to keep path lengths from impacting decisions

## Slide 39: This isn’t the end of the story…
ASes may have more complex business relationships
  Geographic relationships
    E.g., peer in one region, provider in another
  Per-prefix relationships
    E.g., Amazon announcing a prefix to a specific provider
      AS14618 enterprise portion of Amazon
14618
16509
4755
2914
6453

## Slide 40: The outputs ….
15412 12041 p2c
15412 12486 p2c
15412 12880 p2c
15412 13810 p2c
15412 15802 p2c
15412 17408 p2c
15412 17554 p2c
15412 17709 p2c
15412 18101 p2c
15412 19806 p2c
19809 p2c
…

## Slide 41: Outline
Internet Connectivity
  The shift from hierarchy to flat
  Measuring the shift
IXPs
  Based on slides by A. Feldmann

## Slide 42: How do ASes connect?
Point of Presence (PoP)
  Usually a room or a building (windowless)
  One router from one AS is physically connected to the other
  Often in big cities
  Establishing a new connection at PoPs can be expensive
Internet eXchange Points
  Facilities dedicated to providing presence and connectivity for large numbers of ASes
  Many fewer IXPs than PoPs
  Economies of scale

## Slide 43: IXPs Definition
Industry definition (according to Euro-IX)
  A physical network infrastructure operated by a single entity with the purpose to facilitate the exchange of Internet traffic between Autonomous Systems
  The number of Autonomous Systems connected should be at least three and there must be a clear and open policy for others to join.
  https://www.euro-ix.net/what-is-an-ixp

## Slide 44: Internet eXchange Points

## Slide 45: IXPs worldwide
https://prefix.pch.net/applications/ixpdir/

## Slide 46: Inside an IXP

## Slide 47: Inside an IXP
Connection fabric
  Can provide illusion of all-to-all connectivity
  Lots of routers and cables
Also a route server
  Collects and distributes routes from participants

## Slide 48: Structure
IXPs offer connectivity to ASes enable peering

## Slide 49: IXPs -- Peering
Peering – Why? E.g., Giganews:
  “Establishing open peering arrangements at neutral Internet Exchange Points is a highly desirable practice because the Internet Exchange members are able to significantly improve latency, bandwidth, fault-tolerance, and the routing of traffic between themselves at no additional costs.”
IXPs – Four types of peering policies
  Open Peering – inclination to peer with anyone, anywhere
    Most common!
  Selective Peering – Inclination to peer, with some conditions
  Restrictive Peering – Inclination not to peer with any more entities
  No Peering – No, prefer to sell transit
  http://drpeering.net/white-papers/Peering-Policies/Peering-Policy.html

## Slide 50: IXPs – Publicly available information

## Slide 51: IXPs- Publicly available information
Unknown: # of peerings at IXPs

## Slide 52: Peering links – Current Estimates?

## Slide 53: Reading on Web page (Ager et al. SIGCOMM 2012)
Data from a major European IXP
9 months of sFlow records collected in 2011

## Slide 54: IXP Members/participants

## Slide 55: How much traffic is at IXPs?*
We don’t know for sure!
  Seems to be a lot, though.
  One estimate: 43% of exchanged bytes are not visible to us
  Also 70% of peerings are invisible
*Mainly borrowed stolen from Feldmann 2012

## Slide 56: IXP peerings

## Slide 57: Public view of IXP peerings

## Slide 58: Visibility of IXP peerings

## Slide 59: Interesting observations

## Slide 60: Interesting observations (2)

## Slide 61: Revised model 2012+