## Slide 1: CSE 390 – Advanced Computer Networks
Lecture 5: Network Layer
(Putting the Net in Internet)
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 2: Reminders/logistics
Assignment 1 due today. Submit in class or bring to my office.
Assignment 2 coming soon…
Expect more information about assignment environment by Friday
  1 VM per student; Brian Tria will coordinate with you by Friday.

## Slide 3: Network Layer
Function:
  Route packets end-to-end on a network, through multiple hops
Key challenge:
  How to represent addresses
  How to route packets
    Scalability
    Convergence
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 4: Routers, Revisited
How to connect multiple LANs?
LANs may be incompatible
  Ethernet, Wifi, etc…
Connected networks form an internetwork
  The Internet is the best known example
Routers

## Slide 5: Structure of the Internet
Ad-hoc interconnection of networks
  No organized topology
  Vastly different technologies, link capacities
Packets travel end-to-end by hopping through networks
  Routers “peer” (connect) different networks
  Different packets may take different routes
Network 2
Network 1
Network 3
Network 4

## Slide 6: Internetworking Issues
Naming / Addressing
  How do you designate hosts?
Routing
  Must be scalable (i.e. a switched Internet won’t work)
Service Model
  What gets sent?
  How fast will it go?
  What happens if there are failures?
  Must deal with heterogeneity
    Remember, every network is different
Internet Service Model
Best-effort (i.e. things may break)
Store-and-forward datagram network
Lowest common denominator

## Slide 7: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 8: Possible Addressing Schemes
Flat
  e.g. each host is identified by a 48-bit MAC address
  Router needs an entry for every host in the world
    Too big
    Too hard to maintain (hosts come and go all the time)
    Too slow (more later)
Hierarchy
  Addresses broken down into segments
  Each segment has a different level of specificity
Notes: If time, show correlation between lookup speed and maximum line rate

## Slide 9: Example: Telephone Numbers
1-617-373-1234
West Village H
Room 256
Very General
Very Specific
West Village G
Room 1234
3278
Updates are Local

## Slide 10: Binary Hierarchy Example
1**
10*
11*
100
101
110
111
0**
00*
01*
000
001
010
011
Datagram, Destination = 101

## Slide 11: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g. 192.168.21.76
  Each number is a byte
  Stored in Big Endian order
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31

## Slide 12: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
  Too slow: 48GE ports and 4x10GE needs 176Gbps bandwidth DRAM: ~1-6 Gbps; TCAM is fast, but 400x cost of DRAM
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers

## Slide 13: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: NEU
129.10.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24

## Slide 14: How Do You Get IPs?
IP address ranges controlled by IANA
  Internet Assigned Number Authority
  Roots go back to 1972, ARPANET, UCLA
  Today, part of ICANN
IANA grants IPs to regional authorities
  ARIN (American Registry of Internet Numbers) may grant you a range of IPs
  You may then advertise routes to your new IP range
  There are now secondary markets, auctions, …

## Slide 15: Two Level Hierarchy
…
…
Host
Network
Subtree size determined by network class
Pfx

## Slide 16: Class Sizes
Class | Prefix Bits | Network Bits | Number of Classes | Hosts per Class
A | 1 | 7 | 27 – 2 = 126 (0 and 127 are reserved) | 224 – 2 = 16,777,214 (All 0 and all 1 are reserved)
B | 2 | 14 | 214 = 16,398 | 216 – 2 = 65,534 (All 0 and all 1 are reserved)
C | 3 | 21 | 221 = 2,097,512 | 28 – 2 = 254 (All 0 and all 1 are reserved)
 |  |  | Total: 2,114,036 | 
Too many network IDs
Too small to be useful
Way too big

## Slide 17: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:

## Slide 18: Subnet Example
Extract network:
Extract host:
10110101 11011101 01010100 01110010
IP Address:
& 11111111 11111111 11000000 00000000
Subnet Mask:
10110101 11011101 01000000 00000000
Result:
10110101 11011101 01010100 01110010
IP Address:
& ~(11111111 11111111 11000000 00000000)
Subnet Mask:
00000000 00000000 00010100 01110010
Result:

## Slide 19: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks

## Slide 20: Example Routing Table
Address Pattern | Subnet Mask | Destination Router
0.0.0.0 | 0.0.0.0 | Router 4
18.0.0.0 | 255.0.0.0 | Router 2
128.42.0.0 | 255.255.0.0 | Router 3
128.42.128.0 | 255.255.128.0 | Router 5
128.42.222.0 | 2555.255.255.0 | Router 1
Question: 128.42.222.198 matches four rows
  Which router do we forward to?
Longest prefix matching
  Use the row with the longest number of 1’s in the mask
  This is the most specific match

## Slide 21: Subnetting Revisited
Question: does subnetting solve all the problems of class-based routing?
NO
Classes are still too coarse
  Class A can be subnetted, but only 126 available
  Class C is too small
  Class B is nice, but there are only 16,398 available
Routing tables are still too big
  2.1 million entries per router

## Slide 22: Classless Inter Domain Routing
CIDR, pronounced ‘cider’
Key ideas:
  Get rid of IP classes
  Use bitmasks for all levels of routing
  Aggregation to minimize FIB (forwarding information base)
Arbitrary split between network and host
  Specified as a bitmask or prefix length
  Example: Northeastern
    129.10.0.0 with netmask 255.255.0.0
    129.10.0.0 / 16

## Slide 23: Aggregation with CIDR
Original use: aggregating class C ranges
One organization given contiguous class C ranges
  Example: Microsoft, 207.46.192.* – 207.46.255.*
  Represents 26 = 64 class C ranges
  Specified as CIDR address 207.46.192.0/18
11001111
CF
207
00101110
2E
46
11xxxxxx
C0
192
xxxxxxxx
00
0
Decimal
Hex
Binary
0
8
16
24
31
18 Bits Frozen By Netmask
14 Arbitrary Bits

## Slide 24: Example CIDR Routing Table
Address | Netmask | Third Byte | Byte Range
207.46.0.0 | 19 | 000xxxxx | 0 – 31
207.46.32.0 | 19 | 001xxxxx | 32 – 63
207.46.64.0 | 19 | 010xxxxx | 64 – 95
207.46.128.0 | 18 | 10xxxxxx | 128 – 191
207.46.192.0 | 18 | 11xxxxxx | 192 – 255
Hole in the Routing Table: No coverage for 96 – 127
207.46.96.0/19

## Slide 25: Size of CIDR Routing Tables
From www.cidr-report.org
CIDR has kept IP routing table sizes in check
  Currently ~500,000 entries for a complete IP routing table
  Only required by backbone routers

## Slide 26: We had a special day this summer!
512K day – August 12, 2014
Default threshold size for IPv4 route data in older Cisco routers  512K routes
  Some routers failed over to slower memory
    RAM vs. CAM (content addressable memory)
  Some routes dropped
Cisco issues update in May anticipating this issue
  Reallocated some IPv6 space for IPv4 routes
http://cacm.acm.org/news/178293-internet-routing-failures-bring-architecture-changes-back-to-the-table/fulltext

## Slide 27: Causes and solutions
Traffic engineering
  Sometimes I want to announce different prefixes to different neighbors (e.g., use multiple longer prefixes)
Security
  E.g., announce two /9s in addition to a /8 to help prevent dark-space hijacks
New markets
  New networks in regions like Africa, Middle East, etc. with their own prefixes
Solutions
  Stop-gap: update router to reallocate IPv6 memory
  Route aggregation/prefix filtering
  Upgrade routers with more memory ($$$$)

## Slide 28: Takeaways
Hierarchical addressing is critical for scalability
  Not all routers need all information
  Limited number of routers need to know about changes
Non-uniform hierarchy useful for heterogeneous networks
  Class-based addressing is too course
  CIDR improves scalability and granularity
Implementation challenges
  Longest prefix matching is more difficult than schemes with no ambiguity

## Slide 29: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 30: IP Datagrams
IP Datagrams are like a letter
  Totally self-contained
  Include all necessary addressing information
  No advanced setup of connections or circuits
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 31: IP Header Fields: Word 1
Version: 4 for IPv4
Header Length: Number of 32-bit words (usually 5)
Type of Service: Priority information (unused)
Datagram Length: Length of header + data in bytes
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
Limits packets to 65,535 bytes

## Slide 32: IP Header Fields: Word 3
Time to Live: decremented by each router
  Used to kill looping packets
Protocol: ID of encapsulated protocol
  6 = TCP, 17 = UDP
Checksum
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
Used to implement trace route

## Slide 33: IP Header Fields: Word 4 and 5
Source and destination address
  In theory, must be globally unique
  In practice, this is often violated
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 34: Problem: Fragmentation
Problem: each network has its own MTU
  DARPA principles: networks allowed to be heterogeneous
  Minimum MTU may not be known for a given path
IP Solution: fragmentation
  Split datagrams into pieces when MTU is reduced
  Reassemble original datagram at the receiver
MTU = 2000
MTU = 4000
MTU = 1500
Datagram
Dgram1
Dgram2
1
2
3
4

## Slide 35: IP Header Fields: Word 2
Identifier: a unique number for the original datagram
Flags: M flag, i.e. this is the last fragment
Offset: byte position of the first byte in the fragment
  Divided by 8
Version
HLen
TOS
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 36: Fragmentation Example
MTU = 2000
MTU = 4000
MTU = 1500
Data
Data
Data
IP Hdr
IP
IP
Length = 3820, M = 0
3800
20
Length = 2000, M = 1
Offset = 0
Length = 1840, M = 0
Offset = 1980
1980
20
1820
20
1980
+ 1820
= 3800

## Slide 37: Fragmentation Example
MTU = 2000
MTU = 1500
Data
Data
IP
IP
Data
Data
IP
IP
Length = 2000, M = 1
Offset = 0
Length = 1840, M = 0
Offset = 1980
1980
20
1820
20
20
20
1480
500
Length = 520, M = 1
Offset = 1480
Length = 1500, M = 1
Offset = 0
Data
Data
IP
IP
20
20
1480
340
Length = 360, M = 0
Offset = 3460
Length = 1500, M = 1
Offset = 1980
1480
+ 500
= 1980

## Slide 38: IP Fragment Reassembly
Performed at destination
M = 0 fragment gives us total data size
  360 – 20 + 3460 = 3800
Challenges:
  Out-of-order fragments
  Duplicate fragments
  Missing fragments
Basically, memory management nightmare
Data
IP
20
1480
Data
IP
20
500
Length = 520, M = 1, Offset = 1480
Length = 1500, M = 1, Offset = 0
Data
IP
20
1480
Data
IP
20
340
Length = 360, M = 0, Offset = 3460
Length = 1500, M = 1, Offset = 1980

## Slide 39: Fragmentation Concepts
Highlights many key Internet characteristics
  Decentralized and heterogeneous
    Each network may choose its own MTU
  Connectionless datagram protocol
    Each fragment contains full routing information
    Fragments can travel independently, on different paths
  Best effort network
    Routers/receiver may silently drop fragments
    No requirement to alert the sender
  Most work is done at the endpoints
    i.e. reassembly

## Slide 40: Fragmentation in Reality
Fragmentation is expensive
  Memory and CPU overhead for datagram reconstruction
  Want to avoid fragmentation if possible
MTU discovery protocol
  Send a packet with “don’t fragment” bit set
  Keep decreasing message length until one arrives
  May get “can’t fragment” error from a router, which will explicitly state the supported MTU
Router handling of fragments
  Fast, specialized hardware handles the common case
  Dedicated, general purpose CPU just for handling fragments

## Slide 41: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 42: The IPv4 Address Space Crisis
Problem: the IPv4 address space is too small
  232 = 4,294,967,296 possible addresses
  Less than one IP per person
Parts of the world have already run out of addresses
  IANA assigned the last /8 block of addresses in 2011
Region | Regional Internet Registry (RIR) | Exhaustion Date
Asia/Pacific | APNIC | April 19, 2011
Europe/Middle East | RIPE | September 14, 2012
North America | ARIN | 13 Jan 2015 (Projected)
South America | LACNIC | 13 Jan 2015 (Projected)
Africa | AFRINIC | 17 Jan 2022(Projected)

## Slide 43: IPv6
IPv6, first introduced in 1998(!)
  128-bit addresses
  4.8 * 1028 addresses per person
Address format
  8 groups of 16-bit values, separated by ‘:’
  Leading zeroes in each group may be omitted
  Groups of zeroes can be omitted using ‘::’
  2001:0db8:0000:0000:0000:ff00:0042:8329
  2001:0db8:0:0:0:ff00:42:8329
  2001:0db8::ff00:42:8329

## Slide 44: IPv6 Trivia
Who knows the IP for localhost?
  127.0.0.1
What is localhost in IPv6?
  ::1

## Slide 45: IPv6 Header
Double the size of IPv4 (320 bits vs. 160 bits)
Version
DSCP/ECN
Flow Label
0
8
16
24
31
4
12
19
Datagram Length
Next Header
Hop Limit
Source IP Address
Destination IP Address
Version = 6
Groups packets into flows, used for QoS
Same as IPv4
Same as Protocol in IPv4
Same as TTL in IPv4
Same as IPv4

## Slide 46: Differences from IPv4 Header
Several header fields are missing in IPv6
  Header length – rolled into Next Header field
  Checksum – was useless, so why keep it
  Identifier, Flags, Offset
    IPv6 routers do not support fragmentation
    Hosts are expected to use path MTU discovery
Reflects changing Internet priorities
  Today’s networks are more homogeneous
  Instead, routing cost and complexity dominate

## Slide 47: Performance Improvements
No checksums to verify
No need for routers to handle fragmentation
Simplified routing table design
  Address space is huge
  No need for CIDR (but need for aggregation)
  Standard subnet size is 264 addresses
Simplified auto-configuration
  Neighbor Discovery Protocol
  Used by hosts to determine network ID
  Host ID can be random!

## Slide 48: Additional IPv6 Features
Source Routing
  Host specifies the route to wants packet to take
Mobile IP
  Hosts can take their IP with them to other networks
  Use source routing to direct packets
Privacy Extensions
  Randomly generate host identifiers
  Make it difficult to associate one IP to a host
Jumbograms
  Support for 4Gb datagrams

## Slide 49: Deployment Challenges
Switching to IPv6 is a whole-Internet upgrade
  All routers, all hosts
  ICMPv6, DHCPv6, DNSv6
2013: 0.94% of Google traffic was IPv6, 2.5% today
IPv4
TCP, UDP, ICMP
HTTP, FTP, SMTP, RTP, IMAP, …
Ethernet, 802.11x, DOCSIS, …
Fiber, Coax, Twisted Pair, Radio, …

## Slide 50: Transitioning to IPv6
How do we ease the transition from IPv4 to IPv6?
  Today, most network edges are IPv6 ready
    Windows/OSX/iOS/Android all support IPv6
    Your wireless access point probably supports IPv6
  The Internet core is hard to upgrade
  … but a IPv4 core cannot route IPv6 traffic
Core
Internet
Business
Network
Home
Network
IPv6 Ready
IPv6 Ready
IPv4 Only :(
IPv6 Packets

## Slide 51: Transition Technologies
How do you route IPv6 packets over an IPv4 Internet?
Transition Technologies
  Use tunnels to encapsulate and route IPv6 packets over the IPv4 Internet
  Several different implementations
    6to4
    IPv6 Rapid Deployment (6rd)
    Teredo
    … etc.

## Slide 52: 6to4 Basics
Problem: you’ve been assigned an IPv4 address, but you want an IPv6 address
  Your ISP can’t or won’t give you an IPv6 address
  You can’t just arbitrarily choose an IPv6 address
Solution: construct a 6to4 address
  6to4 addresses always start with 2002::
  Embed the 32-bit IPv4 inside the 128-bit IPv6 address
20 02:
207.
CF 2E:
46.
C0 00:
192.
0000
0
IPv4:
IPv6:

## Slide 53: Routing from 6to4 to 6to4
IPv4
Internet
Dest: 16.79.8.0
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv4 – 16.79.8.0
IPv6 – 2002:104F:0800::
Dest: 2002:104F:0800::
How does a host using 6to4 send a packet to another host using 6to4?

## Slide 54: Routing from 6to4 to Native IPv6
IPv4 – 192.88.99.1
IPv6 – 2002:: /16
IPv4
Internet
IPv6
Internet
Dest: 192. 88.99.1
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv6 – 1893:92:13:99::
Dest: 1893:92:13:99::
Special, anycasted IPv4 address for
6to4 Relay Routers
Many ISPs provide 6to4 relay routers

## Slide 55: Routing from Native IPv6 to 6to4
IPv4 – 192.88.99.1
IPv6 – 2002:: /16
IPv4
Internet
IPv6
Internet
Dest: 207.46.192.0
IPv4 – 207.46.192.0
IPv6 – 2002:CF2E:C000::
IPv6 – 1893:92:13:99::
Dest: 2002:CF2E:C000::
Use normal IPv6 routing to reach a 6to4 relay router

## Slide 56: Problems with 6to4
Uniformity
  Not all ISPs have deployed 6to4 relays
Quality of service
  Third-party 6to4 relays are available
  …but, they may be overloaded or unreliable
Reachability
  6to4 doesn’t work if you are behind a NAT
Possible solutions
  IPv6 Rapid Deployment (6rd)
    Each ISP sets up relays for its customers
    Does not leverage the 2002:: address space
  Teredo
    Tunnels IPv6 packets through UDP/IPv4 tunnels
    Can tunnel through NATs, but requires special relays

## Slide 57: Consequences of IPv6
Beware unintended consequences of IPv6
Example: IP blacklists
  Currently, blacklists track IPs of spammers/bots
  Few IPv4 addresses mean list sizes are reasonable
  Hard for spammers/bots to acquire new IPs
Blacklists will not work with IPv6
  Address space is enormous
  Acquiring new IP addresses is trivial