## Slide 1: CSE390 – Advanced Computer Networks
Lecture 22: Software designed networking
Based on slides by J. Rexford @ Princeton & N. Mckeown @ Stanford & S. Shenker @ Berkeley. Updated by P. Gill Fall 2014.

## Slide 2: Data, Control, and Management Planes

## Slide 3: Timescales
 | Data | Control | Management
Time-scale | Packet (nsec) | Event (10 msec to sec) | Human (min to hours)
Tasks | Forwarding, buffering, filtering, scheduling | Routing, circuit set-up | Analysis, configuration
Location | Line-card hardware | Router software | Humans or scripts

## Slide 4: Data and Control Planes
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 5: Data Plane
Streaming algorithms on packets
  Matching on some bits
  Perform some actions
Wide range of functionality
  Forwarding
  Access control
  Mapping header fields
  Traffic monitoring
  Buffering and marking
  Shaping and scheduling
  Deep packet inspection
Switching
Fabric
Processor

## Slide 6: Switch: Match on Destination MAC
MAC addresses are location independent
  Assigned by the vendor of the interface card
  Cannot be aggregated across hosts in LAN
mac1 | 
mac2 | 
mac3 | 
mac4 | 
mac5 | 
host
host
host
...
mac1
mac2
mac3
switch
host
host
mac4
mac5

## Slide 7: Router: Match on IP Prefix
IP addresses grouped into common subnets
  Allocated by ICANN, regional registries, ISPs, and within individual organizations
  Variable-length prefix identified by a mask length
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
Prefixes may be nested. Routers identify the longest matching prefix.

## Slide 8: Forwarding vs. Routing
Forwarding: data plane
  Directing a data packet to an outgoing link
  Individual router using a forwarding table
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Individual router creating a forwarding table

## Slide 9: Example: Shortest-Path Routing
Compute: path costs to all nodes
  From a source u to all other nodes
  Cost of the path through each link
  Next hop along least-cost path to s
3
2
2
1
1
4
1
4
5
3
u
s
6
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)
v
w
y
x
t
z

## Slide 10: Distributed Control Plane
Link-state routing: OSPF, IS-IS
  Flood the entire topology to all nodes
  Each node computes shortest paths
  Dijkstra’s algorithm
10
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t

## Slide 11: Distributed Control Plane
Distance-vector routing: RIP, EIGRP
  Each node computes path cost
  … based on each neighbors’ path cost
  Bellman-Ford algorithm
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) = min{c(u,v) + dv(z),
c(u,w) + dw(z)}

## Slide 12: Traffic Engineering Problem
Management plane: setting the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
3
2
2
1
1
3
1
4
5
3
3

## Slide 13: Traffic Engineering: Optimization
Inputs
  Network topology
  Link capacities
  Traffic matrix
Output
  Link weights
Objective
  Minimize max-utilized link
  Or, minimize a sum of link congestion
3
2
2
1
1
3
1
4
5
3

## Slide 14: Transient Routing Disruptions
Topology changes
  Link weight change
  Node/link failure or recovery
Routing convergence
  Nodes temporarily disagree how to route
  Leading to transient loops and blackholes
1
4
5
3
1
4
10
3
1
4
10
3

## Slide 15: Management Plane Challenges
Indirect control
  Changing weights instead of paths
  Complex optimization problem
Uncoordinated control
  Cannot control which router updates first
Interacting protocols and mechanisms
  Routing and forwarding
  Naming and addressing
  Access control
  Quality of service
  …

## Slide 16: Software Defined Networking (high level view)

## Slide 17: Control/Data Separation
decouple control and data planes by providing open standard API

## Slide 18: (Logically) Centralized Controller
Controller Platform

## Slide 19: Protocols  Applications
Controller Platform
Controller Application

## Slide 20: Outline
What are Software Defined Networks?
Why SDN?
The Consequences
  For industry
  For research
  For standards and protocols

## Slide 21
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Notes: The mainframe industry in the 1980s was vertical and closed: it consisted of specialized hardware, operating system and applications --- all from the same company.
A revolution happened when open interfaces started to appear. The industry became horizontal. Innovation exploded.

## Slide 22
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface
22

## Slide 23
Million of lines of source code
6,000 RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary
Networking industry with “mainframe” mind-set
Custom Hardware
OS
Routing, management, mobility management, access control, VPNs, …
Feature
Feature

## Slide 24: The network is changing
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
OS
OS
OS
OS
OS
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 25: Software Defined Network (SDN)
Feature
Feature
Network OS
1. Open interface to packet forwarding
3. Consistent, up-to-date global network view
2. At least one Network OS probably many. Open- and closed-source
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 26: Network OS
Network OS: distributed system that creates a consistent, up-to-date network view
  Runs on servers (controllers) in the network
  NOX, ONIX, Trema, Beacon, Maestro, … + more
Uses forwarding abstraction to:
  Get state information from forwarding elements
  Give control directives to forwarding elements

## Slide 27: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 28: Control Program
Control program operates on view of network
  Input: global network view (graph/database)
  Output: configuration of each network device
Control program is not a distributed system
  Abstraction hides details of distributed state

## Slide 29: Forwarding Abstraction
Purpose: Abstract away forwarding hardware
Flexible
  Behavior specified by control plane
  Built from basic set of forwarding primitives
Minimal
  Streamlined for speed and low-power
  Control program not vendor-specific
OpenFlow is an example of such an abstraction

## Slide 30: OpenFlow Basics
OpenFlow Protocol
Data Path (Hardware)
Control Path
OpenFlow
Ethernet Switch
Network OS
Control Program A
Control Program B

## Slide 31: OpenFlow Basics
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Flow
Table(s)
“If header = p, send to port 4”
“If header = ?, send to me”
“If header = q, overwrite header with r, add header s, and send to ports 5,6”

## Slide 32: Plumbing Primitives
Primitive is <Match, Action>
Match arbitrary bits in headers:
  Match on any header, or new header
  Allows any flow granularity
Action
  Forward to port(s), drop, send to controller
  Overwrite header with mask, push or pop
  Forward at specific bit-rate
Header
Data
Match: 1000x01xx0101001x
32

## Slide 33: General Forwarding Abstraction
Small set of primitives
“Forwarding instruction set”
Protocol independent
Backward compatible
Switches, routers, WiFi APs, basestations, TDM/WDM

## Slide 34: Example 1: OSPF and Dijkstra
OSPF
  RFC 2328: 245 pages
Distributed System
  Builds consistent, up-to-date map of the network: 101 pages
Dijkstra’s Algorithm
  Operates on map: 4 pages

## Slide 35: Example
OSPF = Dijkstra
IS-IS
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Distributed System
Custom Hardware
OS
OSPF
IS-IS
Distributed
System
Distributed
System

## Slide 36: Outline
What are Software Defined Networks?
Why SDN?
The Consequences
  For industry
  For research
  For standards and protocols

## Slide 37: Great talk by Scott Shenker http://www.youtube.com/watch?v=WVs7Pc99S7w
(Story summarized here)

## Slide 38: Networking
Networking is
  “Intellectually Weak”
  behind other fields
  about the mastery of complexity
Good abstractions tame complexity
  Interfaces are instances of those abstractions
No abstraction => increasing complexity
  We are now at the complexity limit

## Slide 39: By comparison: Programming
Machine languages: no abstractions
  Had to deal with low-level details
Higher-level languages: OS and other abstractions
  File system, virtual memory, abstract data types, ...
Modern languages: even more abstractions
  Object orientation, garbage collection,…

## Slide 40: Programming Analogy
What if programmers had to:
  Specify where each bit was stored
  Explicitly deal with internal communication errors
  Within a programming language with limited expressibility
Programmers would redefine problem by:
  Defining higher level abstractions for memory
  Building on reliable communication primitives
  Using a more general language

## Slide 41: Specification Abstraction
Network OS eases implementation
  E.g., Helps manage distributed state
Next step is to ease specification
  E.g., How do you specify what the system should do?
Key goals
  Provide abstract view of network map
  Control program operates on abstract view
  Develop means to simplify specification

## Slide 42: Software Defined Network (SDN)
Control Program A
Control Program B
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Network OS
Global Network View
Abstract Network View
Virtualization
Consequence:
Work on Nework Programming Languages Pyretic, Frenetic etc.

## Slide 43: Outline
What are Software Defined Networks?
Why SDN?
The Consequences
  For industry
  For research
  For standards and protocols

## Slide 44: SDN in development
Domains
Data centers
Enterprise/campus
Cellular backhaul
Enterprise WiFi
WANs
Products
Switches, routers: About 15 vendors
Software: About 6 vendors and startups
New startups (6 so far). Lots of hiring in networking.

## Slide 45: Open Networking Foundation (ONF)
New non-profit standards organization (Mar 2011)
Defining standards for SDN, starting with OpenFlow
Board of Directors
  Google, Facebook, Microsoft, Yahoo, DT, Verizon
39 Member Companies
  Cisco, VMware, IBM, Juniper, HP, Broadcom, Citrix, NTT, Intel, Ericsson, Dell, Huawei, …
http://www.OpenNetworkingFoundation.org

## Slide 46: Cellular industry
Recently made transition to IP
Billions of mobile users
Need to securely extract payments and hold users accountable
IP is bad at both, yet hard to change
SDN enables industry to customize their network

## Slide 47: Telco Operators
Global IP traffic growing 40-50% per year
End-customer monthly bill remains unchanged
Therefore, CAPEX and OPEX need to reduce 40-50% per Gb/s per year
But in practice, reduces by ~20% per year
SDN enables industry to reduce OPEX and CAPEX
…and to create new differentiating services

## Slide 48: Example: New Data Center
Cost
200,000 servers
Fanout of 20  10,000 switches
$5k vendor switch = $50M
$1k commodity switch = $10M
Savings in 10 data centers = $400M
Control
More flexible control
Tailor network for services
Quickly improve and innovate

## Slide 49: Consequences for research
Ease of trying new ideas
  Existing tools: NOX, Beacon, switches, Mininet
  More rapid technology transfer
  GENI, Ofelia and many more
A stronger foundation to build upon
  Provable properties of forwarding
  New languages and specification tools

## Slide 50: Consequences for standards
Standards will define the interfaces
The role of standards will change:
  Network owners will define network behavior
  Features will be adopted without standards
Programming world
  Good software is adopted, not standardized

## Slide 51: Summary
Networks becoming
  More programmatic
  Defined by owners and operators, not vendors
  Faster changing, to meet operator needs
  Lower opex, capex and power
Abstractions
  Will shield programmers from complexity
  Make behavior more provable
  Will take us places we can’t yet imagine

## Slide 52: Administravia …
Assignment 4 due December 13
Internet in the News (10% of final grade)
  Due next Monday Dec. 1 on Piazza
  Reading/commenting on others’ Internet in the News part of participation mark
  Recent news: http://www.newsweek.com/china-could-shut-down-us-power-grid-cyber-attack-says-nsa-chief-286119
  Lots of topics, pick something you find interesting
No class Wednesday!
Next Monday  Mobile networks!