## Slide 1
Phillipa Gill
University of Toronto
Bernard Wong
Cornell University
Yashar Ganjali & David Lie
University of Toronto
Dude, where’s that IP? Circumventing measurement-based geolocation

## Slide 2: Geolocation applications: Custom content
Local search results
Targeted advertisements

## Slide 3: Geolocation applications: Access control

## Slide 4: Geolocation applications: Fraud prevention
Proof of work [Kaiser and Feng 2010]
  Clients forced to solve computational puzzles,
  Hardness of puzzle based on distance
Online payment fraud
  Use location to flag suspicious transactions

## Slide 5: Behind the scenes
User
(Boston, MA)
Geolocation Database
Web server
128.197.11.23
HTTP GET
[128.197.11.23]
128.197.11.23 ??
Boston, MA
USA
02116
Deny access

## Slide 6: Future application of geolocation
Enforcing regional restrictions in cloud computing
Use geolocation to locate virtual machines

## Slide 7: Motivation
Targets have incentive to lie
Content providers:
  Restrict access to content
  Prevent fraud
Cloud computing users:
  Need the ability to guarantee the result of geolocation

## Slide 8: Our contributions
First to consider measurement-based geolocation of an adversary
Two models of adversarial geolocation targets
  Web client (end host)
  Cloud provider (network)
Evaluation of attacks on
delay and topology-based
geolocation.

## Slide 9: Road map
Motivation & Contributions
Background
Adversary models
Evaluation
Conclusions
Ongoing/Future work

## Slide 10: Geolocation background
Databases/passive approaches
  whois services
  Commercial databases
    Quova, MaxMind, etc.
  Drawbacks:
    coarse-grained
    slow to update
    proxies

## Slide 11: Coarse grained geolocation
traceroute to 74.125.229.18 (Google)
1 80.82.140.226 0.209 ms 0.129 ms 0.328 ms
2 80.82.140.42 0.539 ms 0.525 ms 0.498 ms
3 80.82.140.43 0.472 ms 0.451 ms 0.427 ms
4 195.66.226.125 1.066 ms 1.077 ms 1.075 ms
5 209.85.252.76 1.022 ms 0.943 ms 0.979 ms
6 216.239.43.192 76.558 ms 76.454 ms 75.900 ms
7 209.85.251.9 91.356 ms 93.749 ms 93.941 ms
8 64.233.175.34 92.907 ms 93.624 ms 94.090 ms
9 74.125.229.18 93.307 ms 93.389 ms 90.771 ms
LINX(UK)
Google (USA?)
Notes: Delay difference between LINX and google implies google IP is not in the us!

## Slide 12: Coarse grained geolocation
traceroute to 74.125.229.18 (Google)
1 80.82.140.226 0.209 ms 0.129 ms 0.328 ms
2 80.82.140.42 0.539 ms 0.525 ms 0.498 ms
3 80.82.140.43 0.472 ms 0.451 ms 0.427 ms
4 195.66.226.125 1.066 ms 1.077 ms 1.075 ms
5 209.85.252.76 1.022 ms 0.943 ms 0.979 ms
6 216.239.43.192 76.558 ms 76.454 ms 75.900 ms
7 209.85.251.9 91.356 ms 93.749 ms 93.941 ms
8 64.233.175.34 92.907 ms 93.624 ms 94.090 ms
9 74.125.229.18 93.307 ms 93.389 ms 90.771 ms
LINX(UK)
Google (USA?)

## Slide 13: Delay-based geolocation
Example:
  Constraint-based geolocation [Gueye et al. ToN ‘06]
Ping!
Ping!
Ping!
Ping other landmarks to calibrate
Distance-delay “best-line” function

## Slide 14: Delay-based geolocation
Ping!
2. Ping target
Ping!
Ping!
Ping!
Example
  Constraint-based geolocation [Gueye et al. ToN ‘06]

## Slide 15: Delay-based geolocation
3. Map delay to distance from target
4. Constrain target location
Example
  Constraint-based geolocation [Gueye et al. ToN ‘06]

## Slide 16: Topology-aware geolocation
Delay-based geolocation assumes direct paths
Ping!
“as the crow flies”
Ping!
reality

## Slide 17: Topology-aware geolocation
Takes into account circuitous network paths

## Slide 18: Types of measurement-based geolocation:
Delay-based:
  Constraint-based geolocation (CBG) [Gueye et al. ToN ‘06]
  Computes region where target may be located
  Reported average accuracy: 78-182 km
Topology-aware:
  Octant [Wong et al. NSDI 2007]
  Considers delay between hops on path
  Geolocates nodes along the path
  Reported median accuracy: 35-40 km

## Slide 19: Road map
Motivation & Contributions
Background
Adversary models
Evaluation
Conclusions
Future work

## Slide 20: Simple adversary (e.g., Web client)
Knows the geolocation algorithm
Able to delay their response to probes
  i.e., increase observed delays
Cannot decrease delay
Landmark i

## Slide 21: Sophisticated adversary (e.g., Cloud provider)
Controls the network the target is located in
Network has multiple geographically distributed entry points
Adversary constructs network paths to mislead topology-aware geolocation
tar
landmark
target

## Slide 22: Road map
Motivation & Contributions
Background
Adversary models
Evaluation
Conclusions
Future work

## Slide 23: Evaluation
Questions:
  How accurately can an adversary mislead geolocation?
  Can they be detected?
False location
True location
Geolocation result
Distance of attempted move
Error for the
adversary

## Slide 24: Methodology
Collected traceroutes between 50 PlanetLab nodes
Each node takes turn as target
Each target moved to a set of forged locations
Landmarks
Forged Locations

## Slide 25: Results overview
 | Simple | Sophisticated
Delay-based |  | 
Topology-aware |  | 
Adversary Type
Geolocation method

## Slide 26: Results overview
 | Simple | Sophisticated
Delay-based |  | 
Topology-aware |  | 
Adversary Type
Geolocation method
?
?

## Slide 27: Delay adding attack
Increase delay by time to travel g2-g1
Challenge: how to map distance to delay
Our attack:
  V1: Speed of light approximation
  V2: Adversary knows “best-line” function
g2
g1
False location
True location
Notes: Note this does not work if g2 < g1

## Slide 28: Delay-adding attack
Landmark 1
Landmark 2
Landmark 3

## Slide 29: Delay-adding attack
Landmark 3
Landmark 1
Landmark 2

## Slide 30: Can it be detected?
Area of intersection
increases as delay is added
Abnormally large region sizes can reveal results that have been tampered with

## Slide 31: How accurate can the attack be?
NYC-SFO
700 M/KM
400 M/KM
Trade off between accuracy and detectability

## Slide 32: Results overview
 | Simple | Sophisticated
Delay-based |  | 
Topology-aware |  | 
Adversary Type
Geolocation method
?
Limited Accuracy
Detectable using region size

## Slide 33: Adding delay to topology-aware geolocation
Landmark 1
Landmark 2
Landmark 2 add delay
Landmark 1 add delay

## Slide 34: Adding delay to topology-aware geolocation
Landmark 1
Landmark 2
Landmark 2 add delay
Landmark 1 add delay
Detectable!

## Slide 35: Results overview
 | Simple | Sophisticated
Delay-based |  | 
Topology-aware |  | 
Adversary Type
Geolocation method
Limited Accuracy
Detectable using region size
?

## Slide 36: Hop-adding attack
Sophisticated adversary
  Can alter traceroute paths after they enter the adversary’s network
  Has a WAN with multiple entry points
Challenge: how to design the non-existent paths
Our attack:
  Leverage existing network entry points
  Use a non-existent (simulated) network to generate fake paths

## Slide 37: Hop-adding attack: Simulated network
Multiple network entry points
In-degree 3 for each node
Fake node next to each forged location

## Slide 38: How accurate can the attack be?
Even moving long distances sophisticated adversary has high accuracy
NYC-SFO
Adversary can move from EU to US 100% of the time.

## Slide 39: Can it be detected?
Hop adding is able to mislead the algorithm without increasing region size!
Region size does not increase

## Slide 40: Results overview
 | Simple | Sophisticated
Delay-based |  | 
Topology-aware |  | 
Adversary Type
Geolocation method
Limited Accuracy
Detectable using region size
High accuracy
Difficult to detect

## Slide 41: Road map
Motivation
Background
Adversary models
Evaluation
Conclusions
Future work

## Slide 42: Conclusions
Current geolocation approaches are susceptible to malicious targets
  Databases misled by proxies
  Measurement-based geolocation by attacks on delay and topology measurements
Developed and evaluated adversary models for measurement-based geolocation techniques
Topology-aware geolocation better in benign case, worse in adversarial setting!

## Slide 43: Future work
Develop a framework for secure geolocation
Require the adversary to prove they are in the correct location
Goals:
  Provable security: Upper bound on what an adversary can get away with.
  Practical framework: Should be tolerant of variations in network delay

## Slide 44: Thanks!
Paper appears in: Usenix Security 2010
http://www.cs.toronto.edu/~phillipa
Contact:
phillipa@cs.toronto.edu