## Slide 1: CS590/690 Internet censorship (Spring 2018)
Lecture 02
ACKs: Slides based on material from Nick weaver’s presentation at the connaught summer institute 2013

## Slide 2: What is a network censor
An entity that desires that some identifiable communication is blocked from being transmitted over the network
Without the authority to compel the content provider to remove the content
Without the authority to compel the client to install software of the censor’s choosing
Requires that the censor act on network traffic
Image from Watch, Learn, Drive
http://watch-learn-drive.com/Learners_Online/New_places/Traffic_lights/TL_5.html
Notes: Needs to operate on network traffic. Needs to be efficient and scalable. Censorship systems are like other systems!

## Slide 3: How to identify and block?
Identification: The piece of information that allows the censor to identify content to be blocked is referred to as the censorship trigger
Example: IP address, hostname, URL, keywords etc.
Blocking: The technical means used to restrict access to the content
Example: dropping packets, forging TCP RST packets or DNS responses
In the next few lectures we will be exploring censorship as it exploits different triggers and blocking mechanisms at different layers of the Internet Protocol stack.

## Slide 4: Networking 101
Protocols on the Internet divided into logical layers
These layers work together to get traffic where it is going.
Headers of upper layers encapsulate lower layer protocols
A network censor can disrupt any layer!
Application layer
(DNS, HTTP, HTTPS)
Transport Layer
(TCP, UDP)
Network Layer
(IP, ICMP)
Link Layer
(Ethernet, 802.11)
Physical Layer
(satellite, fiber)
Bit Torrent, Web (Facebook, Twitter)

## Slide 5: Networking 101
So how does our traffic get where its going?
DNS Server
(2.1.2.3)
Web Server
(3.1.2.3)
Home connection
(2.1.2.4)
Each device has an IP
Within a network routes are learned via “interior gateway protocols” (e.g., OSPF, IS-IS )
ISP B
ISP A
ISP C
Between networks border gateway protocol (BGP) is used to exchange routes
C
Prefix: 3.1.2.0/24
C
Prefix: 3.1.2.0/24
B, C
Prefix: 3.1.2.0/24
(2.1.2.5)
2.1.2.5
Prefix: 3.1.2.0/24
Notes: When the user wants to access the Web server they learn the path via BGP.

## Slide 6: Networking 101
…ok but humans don’t request IP addresses
… they want content!
DNS Server
(2.1.2.3)
Web Server
(208.80.154.238)
Home connection
(2.1.2.4)
ISP B
ISP A
ISP C
(2.1.2.5)
DNS QTYPE A
En.wikipedia.org
DNS A
208.80.154.238
SYN
ACK
SYNACK
HTTP GET /wiki/Douglas_MacArthur HTTP 1.1
Host: en.wikipedia.org
HTTP STATUS 200
Content Length: 523
Content Type: text/html
<!DOCTYPE html>
<html lang="en" dir="ltr" class="client-nojs">
<head>
<meta charset="UTF-8" /><title>Douglas MacArthur - Wikipedia, the free encyclopedia</title>
<meta name="generator" content="MediaWiki 1.23wmf10" />

## Slide 7: Many opportunities to censor
Block IP addresses
  IP layer
Block hostnames
  DNS (application layer)
Disrupt TCP flows
  TCP (transport layer)
  Many possible triggers
Disrupt HTTP transfers
  HTTP (application layer)
Will be going through a variety of these today + next few lectures.

## Slide 8: Internet protocol 101
Relevant fields:
IPID: set by the sender of the IP packet. Some OSes increment globally for each IP packet generated by the host; some maintain per flow counters, use a constant or random values.
TTL: counter gets decremented by each hop on the path until it reaches 0 and an ICMP Time Exceeded Message is generated. Useful for probing/locating censors.
Source IP: IP of the sender of this packet
Destination IP: IP of the recipient of this packet

## Slide 9: IP-based blocking
Option 1: Configure routers using an access control list (ACL) to drop traffic to a given IP address.
Drop traffic to:
8.7.198.45
203.98.7.65
46.82.174.68
59.24.3.173
93.46.8.89
Image from Watch, Learn, Drive
http://watch-learn-drive.com/Learners_Online/New_places/Traffic_lights/TL_5.html
Source: 136.159.220.20
Destination: 46.82.174.68
This is an example of in-path blocking
(censor can remove packets)

## Slide 10: IP-based blocking
Option 1: Configure routers using an access control list (ACL) to drop traffic to a given IP address.
Drop traffic to:
8.7.198.45
203.98.7.65
46.82.174.68
59.24.3.173
93.46.8.89
Image from Watch, Learn, Drive
http://watch-learn-drive.com/Learners_Online/New_places/Traffic_lights/TL_5.html
Source: 136.159.220.20
Destination: 46.82.174.70

## Slide 11: IP-Based blocking
Advantages (for the censor)
  Quick and easy to configure
  Routers have efficient techniques for IP matching
Disadvantages
  Need to know the IP
    Easily evadable!
  High collateral damage: IP != Web host
    Noticeable if high profile site is hosted on the same system
    60% of Web servers are hosted with 10,000 or more other Web servers (Shue et al. 2007)
  Location of the censor can be determined from within the censored network
    Just need to traceroute to the blocked IP (use TCP port 80 SYNs in case ACL is selective).
  Can determine location from censored host as well
    Assuming ICMP Time Expired messages are blocked.

## Slide 12: IP-BASED BLOCKING
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
Option 2: Use BGP to block IPs
  February 2008 : Pakistan Telecom hijacks YouTube
Notes: -level of autonomous systems
-e.g., YouTube, AT&T, pakistan telecom
-routing is done on IP addresses, so when someone wants to go to YouTube they get YouTube’s IP address and YouTube announces to the world that they have the ip address and traffic is forwarded towards them. So here multinet would route to it’s provider pakistan telecom that then forwards the traffic on to youtube.
-these networks chosen for a specific reason which is that there was an incident in february 2008 pakistan telecom actually high jacked traffic going to youtube (misconfiguration).
-they announced to the world that they’re youtube and traffic destined to youtube was routed to them
-youtube was unavailable for a couple of hours as operators phone each other to figure out what was going on.

## Slide 13: IP-BASED BLOCKING
  Here’s what should have happened….
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
X
Hijack + drop packets going to YouTube
  Block your own customers.

## Slide 14: IP-BASED BLOCKING
  But here’s what Pakistan ended up doing…
YouTube
Pakistan
Telecom
“The Internet”
Telnor
Pakistan
Aga Khan
University
Multinet
Pakistan
I’m YouTube:
IP 208.65.153.0 / 22
Pakistan
Telecom
No, I’m YouTube!
IP 208.65.153.0 / 24
Notes: Our works focuses on attacks of this flavor..

## Slide 15: Why was the Pakistan incident so bad?
They announced a more specific prefix
  BGP routing is based on longest prefix match
There is no global route authentication in place!
  ISPs should filter announcements from their customers that are clearly wrong
  (As an ISP you should know what IP address space is in use by your customers)
  In reality this is harder than it seems 

## Slide 16: Ip-based blocking
Option 2: BGP route poisoning
Instead of configuring router ACLs, just advertise a bogus route
  Causes routers close to the censor to route traffic to the censor, which just drops the traffic
How to detect this type of censorship?
  BGP looking glass servers in the impacted region
  Sometimes global monitors as well …
Challenges
  Can cause international collateral damage!
  Will block all content on a given prefix
    Could announce a /32 to get a single address but most ISPs will not propagate beyond a /24

## Slide 17: Known users of ip-based blocking
Pakistan using IP-based blocking for YouTube address ranges
  Can interfere with other Google services
China
  Some reports of IP blocking
  Many URLs redirected to small set of IP-addresses, possibly this is the set used for ACLs
UK
  Uses IP blocking of the Pirate Bay’s IP address
Australia
  IP blocking for Melbourne Free University IPs (precise motivation unclear…)
  https://www.eff.org/deeplinks/2013/04/australian-networks-censor-community-education-site
In general, too much collateral damage of IP-based blocking.

## Slide 18: Other uses of ip-based blocking
Internet “kill switches”
Required reading: Analysis of Country-wide Internet Outages Caused by Censorship. Dainotti et al. IMC 2011
Example: Internet shut downs in Egypt + Libya in 2011
Egypt:
  Jan. 25, 2011: protests start in the country
  Government orders service providers to “shut down” the Internet
  Jan. 27 @ 22:34 UTC: several sources report withdrawal in the Internet’s global routing table of almost all routes to Egyptian networks
  This lasted for 5.5 days!
Libya
  Feb. 17, 2011: Protests start in the country
  The government controls most of the country’s communication infrastructure
  Feb. 18 (6.8 hours), 19th (8.3 hrs), March 3rd (3.7 days): Three different connectivity disruptions

## Slide 19: Rough idea what this looks like
National Telco
Regional ISP 1
Regional ISP 2
Rest of Internet
Prefix 1
Prefix 2
ISP 1
Prefix 1
ISP 2
Prefix 2
Nat. Telco, ISP 2
Prefix 2
Nat. Telco, ISP 1
Prefix 1
Withdrawal

## Slide 20: Some Context
Egypt
3165 IPv4 and 6 IPv6 prefixes delegated to Egypt by AfriNIC
They are managed by 51 autonomous systems
Filtering type: BGP only
Libya
13 IPv4 prefixes, no IPv6
3 autonomous systems operate in the country
Filtering type: mix of BGP, packet filtering, satellite signal jamming

## Slide 21: How to measure this?
BGP
  BGP Updates logged by RIPE-NCC RIS + Routeviews at route collectors
Active Traceroute Probing
  CAIDA manages “Archipelago Measurement Infrastructure” (Ark)
  Traceroutes from ~ 80 hosts to all /24 prefixes
Internet Background Radiation
  Traffic received by the UCSD Network Telescope
  … an unallocated /8: represents unsolicited packets (scans, worms, etc.)

## Slide 22: Data selection
IP ranges associated with the country of interest
  Delegations from Regional Internet Registries (RIR)
  Commercial geolocation database
Gather prefixes to be monitored by looking at BGP announcements. For each IP range
  Look up for an exact match of the BGP prefix
  Find all more specific (strict subset, longer) prefixes
  Otherwise, retrieve the longest BGP prefix containing the prefix.

## Slide 23: BGP disconnection in egypt
Synchronization of withdrawals and announcements between Egyptian ASes

## Slide 24: Long lasting effects
Path changes. These plots generated using BGPlay

## Slide 25: BGP cannot take down satellite links
Probable signal jamming!
Third Libyan outage. SatAS1 was BGP-reachable, only small amount of traffic reaches the telescope

## Slide 26: Advantages of multiple data sets
Telescope (top plot) shows traffic decreasing to nearly 0, while BGP data (bottom plot) shows prefixes are still reachable.
 Packet level filtering/satellite jamming in use

## Slide 27: Hands-on activity
Look up Dyn reports of country-wide outages (eg., Sudan, Libya, Egypt) or censorship-related incidents (eg., Pakistan, China Telecom 2010 incident)
https://dyn.com/blog/
Load BGPPlay data from around the time of the incident. What can you see?
http://bgplay.routeviews.org/ (you will need Java)
Post interesting screen shots from BGPlay to Piazza!
  Alternative BGPPlay Source:
    https://stat.ripe.net/
    Look up the impacted prefixes and ASNs

## Slide 28: Next time …
We continue our journey up the protocol stack with blocking at the transport layer