## Slide 1: CS590B/690B Detecting Network Interference
Lecture 15
Phillipa Gill – Umass Amherst

## Slide 2: Where we are
Last time:
Tor relay-based attacks/Web site fingerprinting
Today:
Timing attacks + Internet routing review
RAPTor

## Slide 3: Anonymity on the Internet
Challenge: By observing Internet traffic one can infer who is talking to whom
  Meta data is the message!
  Track communications over time…
    …behaviors, interests, activities
Tor aims to solve this:
Tor
Does not know source
Does not know destination
Notes: One of the challenges of the Intenret is that it was not designed with anonymity in mind. So somebody observing network traffic can observe the source and destination of each connection and learn about what sites people are visiting even if the connection is encrypted.
As we’ve seen with the NSA revelations in recent years even this sort of meta data about who talks to who can be incredibly valuable for tracking peoples behaviors intersts and activities.
Tor is a system that tries to resolve this issue by providing users an anonymous way to access content online. It does this using encryption and by bouncing the users traffic off of three relays or Tor routers refered to as the entry, middle and exit relay. The basic idea is that someone observing at the entry relay only learns the identify of the source but not the destination and the exit knows the destination but not the source.
On the Internet, by default there is no anonymity, someone observing packets can easily observe the source and destination of the connection and infer who is talking to whom, even if they use encryption .
And as we’ve seen with the NSA relevations this meta data is actually quite critical, you can track communications, behaviors, interests and so on.
So what systems like to try to do is provide users with the ability to use the internet in an anonymous way.

## Slide 4: Tor 101
Tor
Entry
Exit
Middle
Tor circuit is constructed out of three Tor routers/relays
Client iteratively tunnels and exchanges keys with the relays
Notes: Constructs the path out of three Tor routers/relays.
- HOW ARE RELAYS chosen?  based on capacity/load ; limited set of entry relays to mitigate relay-based attacks
Client iteratively exchanges keys with relays on the path and tunnels to the next relay
- When the relay decrypts the message it learns the identity of the next hop on the path. In this way each relay only learns the hop before it and after it in the circuit.
- exit see the actual traffic so if the data contains information about the client the exit can learn who it is.  Tor browser is important.

## Slide 5: Threat model
Tor
Entry
Exit
Middle
Relay-based attacks
Finger print Web sites based on packet timing
Exit relay can observe users’ traffic
(Lots of work on this)
Network-based attacks
Timing attacks can deanonymize users
Actually being tried by gov’t agencies!
(Today’s lecture)
Which user is visiting the site?
Internet routing dynamics make timing attacks easier than you’d think!
Notes: Constructs the path out of three Tor routers/relays.
- HOW ARE RELAYS chosen?  based on capacity/load
Client iteratively exchanges keys with relays on the path and tunnels to the next relay
- When the relay decrypts the message it learns the identity of the next hop on the path. In this way each relay only learns the hop before it and after it in the circuit.
- exit see the actual traffic so if the data contains information about the client the exit can learn who it is.  Tor browser is important.

## Slide 6: AS Numbers
Each AS identified by an ASN number
  16-bit values (latest protocol supports 32-bit ones)
  64512 – 65535 are reserved
Currently, there are ~ 40000 ASNs
  AT&T: 5074, 6341, 7018, …
  Sprint: 1239, 1240, 6211, 6242, …
  Google 15169, 36561 (formerly YT), + others
  Facebook 32934
  North America ASs  ftp://ftp.arin.net/info/asn.txt

## Slide 7: BGP: The Internet’s Routing Protocol (1)
ISP 1
Verizon
Wireless
stub
$
$
$
ISP 2
Level 3
$
$
Stub
(customer)
ISP 2
(provider)
ISP 1
(peer)
Level 3
(peer)
22394
(also VZW)
A simple model of AS-level business relationships.
Notes: In this work we look at issues relating to security of routing on the internet, but first lets see what we mean when we talk about routing.
In this work we focus on routing between autonomous systems on the internet. So you can think of autonomous systems as the network run by an organization. So for example, AT&T’s network might be one autonomous system and the university of toronto’s network is another autonomous system.
Say the prefix is a block of ip addresses
Define AS
This topology corresponds to:
Large ISP 1 = ATT
Large ISP 2 = NTT
Verizon wireless is really “6167 --- 22394”
We have routeviews announcements for ATT and NTT below
======================= ATT = “Large ISP 1” FIXES THINGS ==============
updates.20100408.1600.lines: | TIME: 04/08/10 12:02:49 | TYPE: BGP4MP/MESSAGE/Update | FROM: 12.0.1.63 AS7018 | TO: 128.223.51.102 AS6447 | ORIGIN: IGP | ASPATH: 7018 3356 6167 22394 22394 | NEXT_HOP: 12.0.1.63 | COMMUNITY: 7018:5000 | ANNOUNCE | 72.103.0.0/19 | 166.180.96.0/19 | 66.174.161.0/24 | 166.180.115.0/24 | 166.153.208.0/20 | 166.180.119.0/24 | 166.153.38.0/24 | 166.145.112.0/20 | 166.145.118.0/24 | 166.145.48.0/24 | 70.203.128.0/20 | 166.145.16.0/24 | 166.180.192.0/19 | 166.145.22.0/24 | 70.201.0.0/19 | 70.204.128.0/20 | 151.144.43.0/24 | 151.144.144.0/24 | 166.145.44.0/24 | 166.153.40.0/24 | 66.174.56.0/24 | 166.180.193.0/24 | 151.144.95.0/24 | 166.145.117.0/24 | 70.205.0.0/18 | 70.200.128.0/19 | 166.145.12.0/24 | 166.145.116.0/24 | 151.144.46.0/24 | 166.180.240.0/24 | 166.153.33.0/24 | 72.103.32.0/20 | 70.205.192.0/19 | 166.153.176.0/24 | 166.153.36.0/24 | 166.145.54.0/24 | 166.180.224.0/24 | 166.180.225.0/24 | 166.180.249.0/24 | 166.180.243.0/24 | 166.180.195.0/24 | 166.180.251.0/24 | 166.180.230.0/24 | 166.180.229.0/24 | 166.180.197.0/24 | 166.180.234.0/24 | 166.180.250.0/24 | 166.180.235.0/24 | 166.180.233.0/24 | 166.180.245.0/24 | 166.180.226.0/24 | 166.180.227.0/24 | 166.180.242.0/24 | 166.180.241.0/24 | 166.180.238.0/24 | 166.180.194.0/24 | 166.180.246.0/24 | 166.180.196.0/24 | 151.144.47.0/24
And
================== NTT = “Large ISP 2” fixes things
updates.20100408.1549.lines: | TIME: 04/08/10 11:58:59 | TYPE: BGP4MP/MESSAGE/Update | FROM: 195.66.224.138 AS2914 | TO: 195.66.225.222 AS6447 | ORIGIN: IGP | ASPATH: 2914 3356 6167 22394 22394 | NEXT_HOP: 195.66.224.138 | MULTI_EXIT_DISC: 5 | COMMUNITY: 2914:420 2914:2201 2914:3200 65504:3356 | ANNOUNCE | 66.174.161.0/24 | 66.174.56.0/24

## Slide 8: Standard model of Internet routing
Proposed by Gao & Rexford 12 years ago
Based on practices employed by a large ISP
Provide an intuitive model of path selection and export policy
Path Selection:
1. LocalPref: Prefer customer paths
over peer paths
over provider paths
2. Prefer shorter paths
3. Arbitrary tiebreak
ISP
Customer
Peer
Provider
$
$
$
Notes: The model provides a simple view of how paths are selected and exported to neighboring ASes. The goal of the model isn’t to faithfully capture the behavior of all 36000 ASes on the Internet but to capture the general trend of how routing is done. Part of my goal here today is to understand whether this model holds for the majority of networks and if there are notable exceptions that should be taken into account.
The standard routing policy model was proposed by Gao and Rexford 12 years ago and was based on common practices at a large isp at the time. It breaks routing down into the path selection and export policies.
In terms of path selection, the business relationships between ISPs are modeled as either customer that pays the ISP, peer that the ISP engages in settlement free peering with, or provider that the ISP has to pay. Here you can think of the arrows in this diagram as “where the money flows”
When choosing a path the ISP will prefer to route to a customer, over a peer over a provider. Basically they want to route towards the AS that will pay them using LocalPref.
If they have multiple paths with the same LocalPref the model then says they will prefer a shorter path. And beyond that it goes to arbitrary tiebreak (since we don’t have a notion of intra-domain routing/MEDs here).

## Slide 9: Standard model of Internet routing
Proposed by Gao & Rexford 12 years ago
Based on practices employed by a large ISP
Provide an intuitive model of path selection and export policy
Path Selection:
1. LocalPref: Prefer customer paths
over peer paths
over provider paths
2. Prefer shorter paths
3. Arbitrary tiebreak
Export Policy:
Export customer path
  to all neighbors.
Export peer/provider path
to all customers.
Customer
$
$
Provider
ISP
Provider
$
Announcements
Notes: The export policy is based on ensuring that networks only transit traffic that generates revenue for them.
So if a customer sends them a path they will announce it to all neighbors but if they receive a path from a non customer they will only export it to their customer.

## Slide 10: Timing attacks & routing
Source AS
AS1
AS2
AS3
AS4
Entry relay
Exit relay
Destination AS
$
Customer
Provider
$
Peer
Peer
Internet routing is based on business relationships!
Notes: This slide shows the location of the source, entry, exit and destination on the Internet. Here we are considering routing at the AS level. You can think of an AS …
-- when I talk about routing here I’m talking about routing at the level of autonomous systems, you can think of an autonomous system as a network under control of a single organization, for example AT&T or stony brook university.
-- the client’s traffic will traverse an Internet path consisting of multiple autonomous systems on its way into and out of Tor.

## Slide 11: Timing attacks & routing
Source AS
AS1
AS2
AS3
AS4
Entry relay
Exit relay
Destination AS
ASes prefer cheaper paths!
AS2
Asymmetric routing makes things worse!
ACK #s leak information!
AS3
Insecurity of BGP makes
things even worse!
Notes: However, properties of the internet’s routing system actually make this worse. Specifically traffic from the entry back to the client and from the destination to exit may actually take different paths. Using ack numbers an AS that lies on these reverse paths is also in a position to carry out correlation attacks. For example if we take reverse paths into consideration now AS 3 can also perform the attack.

## Slide 12: IP Address Ownership and Hijacking
IP address block assignment
  Regional Internet Registries (ARIN, RIPE, APNIC)
  Internet Service Providers
Proper origination of a prefix into BGP
  By the AS who owns the prefix
  … or, by its upstream provider(s) in its behalf
However, what’s to stop someone else?
  Prefix hijacking: another AS originates the prefix
  BGP does not verify that the AS is authorized
  Registries of prefix ownership are inaccurate

## Slide 13: How to Hijack a Prefix
The hijacking AS has
  Router with eBGP session(s)
  Configured to originate the prefix
Getting access to the router
  Network operator makes configuration mistake
  Disgruntled operator launches an attack
  Outsider breaks in to the router and reconfigures
Getting other ASes to believe bogus route
  Neighbor ASes not filtering the routes
  … e.g., by allowing only expected prefixes
  But, specifying filters on peering links is hard

## Slide 14: How can hijacks/interception be used to compromise Tor?
Reading presentation: RAPTor
  https://www.usenix.org/conference/usenixsecurity15/technical-sessions/presentation/sun
Murdoch + Danezis

## Slide 15: Exercise
How might we harden Tor against RAPTor attacks?
What sources of data might we leverage?
  Active measurements? (traceroute from client to relays?)
  BGP monitor data?
    How to detect suspicious/hijacking activity?
Which parts of this make sense to implement on the client?
What makes outsourcing functionality (e.g., to a central point) challenging?