## Slide 1: Let the Market Drive Deployment A Strategy for Transitioning to BGP Security
Phillipa Gill
University of Toronto
Sharon Goldberg
Boston University
Michael Schapira
Hebrew University of Jerusalem
& Google NYC
Columbia University
New York, NY
Nov. 17, 2011

## Slide 2: Incentives for BGP Security
Insecurity of Internet routing is well known:
S-BGP proposed in 1997 to address many issues
…but no deployment yet.
Challenges to deployment are being surmounted:
  Political: Rollout of RPKI as a cryptographic root trust
  Technical: Lots of activity in the IETF SIDR working group, DHS, FCC etc.
The pessimistic view:
This is economically infeasible!
Why should ISPs bother deploying S*BGP?
No security benefits until many other ASes deploy!
Worse yet, they can’t make money from it!
Our view:
Calm down. Things aren’t so bad.
ISPs can use S*BGP to make money.

## Slide 3: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 4: BGP: The Internet’s Routing Protocol (1)
ISP 1
Verizon
Wireless
stub
$
$
$
ISP 2
Level 3
$
$
Stub
(customer)
ISP 2
(provider)
ISP 1
(peer)
Level 3
(peer)
22394
(also VZW)
A simple model of AS-level business relationships.

## Slide 5: BGP: The Internet’s Routing Protocol (2)
ISP 1
Verizon
Wireless
ISP 2
Level 3
$
$
  ISP
  ISP
22394
  A stub is an AS with no customers that never transits traffic.
  (Transit = carry traffic from one neighbor to another)
  85% of ASes are stubs!
  We call the rest (15%) ISPs.
X
Loses $
stub

## Slide 6: BGP: The Internet’s Routing Protocol (3)
China
Telecom
ISP 1
Verizon
Wireless
Level 3
Level3, VZW, 22394 66.174.161.0/24
22394
66.174.161.0/24
VZW, 22394 66.174.161.0/24
22394 66.174.161.0/24
Paths chosen based on cost and length.

## Slide 7: Traffic Attraction & Interception Attacks
ChinaTel path is shorter
?
China
Telecom
ISP 1
Verizon
Wireless
Level 3
ChinaTel 66.174.161.0/24
Level3, VZW, 22394 66.174.161.0/24
22394
  This prefix and 50K others were announced by China Telecom
  Traffic for some prefixes was possibly intercepted
  April 2010 : China Telecom intercepts traffic
66.174.161.0/24

## Slide 8: Securing the Internet: RPKI
  Resource Public Key Infrastructure (RPKI): Certified mapping from ASes to public keys and IP prefixes.
China
Telecom
ISP 1
Verizon
Wireless
Level 3
ChinaTel 66.174.161.0/24
?
Level3, VZW, 22394 66.174.161.0/24
22394
X
RPKI: Invalid!
  RPKI shows China Telecom is not a valid origin for this prefix.
66.174.161.0/24

## Slide 9: But RPKI alone is not enough!
  Resource Public Key Infrastructure (RPKI): Certified mapping from ASes to public keys and IP prefixes.
China
Telecom
ISP 1
Verizon
Wireless
Level 3
ChinaTel, 22394 66.174.161.0/24
?
Level3, VZW, 22394 66.174.161.0/24
22394
  Malicious router can pretend to connect to the valid origin.
66.174.161.0/24

## Slide 10: To stop this attack, we need S*BGP (e.g. S-BGP/soBGP) (1)
China
Telecom
ISP 1
Verizon
Wireless
Level 3
22394
VZW: (22394, Prefix)
Level3: (VZW, 22394, Prefix)
VZW: (22394, Prefix)
Public Key Signature: Anyone with 22394’s public key can validate that the message was sent by 22394.
  S-BGP [1997]: RPKI + Cannot announce a path that was not announced to you.
VZW: (22394, Prefix)
Level3: (VZW, 22394, Prefix)
ISP 1: (Level3, VZW, 22394, Prefix)

## Slide 11: To stop this attack, we need S*BGP (e.g. S-BGP/soBGP) (2)
China
Telecom
ISP 1
Verizon
Wireless
Level 3
22394
VZW: (22394, Prefix)
Level3: (VZW, 22394, Prefix)
ISP 1: (Level3, VZW, 22394, Prefix)
  Malicious router can’t announce a direct path to 22394, since 22394 never said
ChinaTel: (22394, Prefix)
  S-BGP [1997]: RPKI + Cannot announce a path that was not announced to you.

## Slide 12: S*BGP must impact route selection
It is not enough to sign and verify
  If we want security, S*BGP must impact BGP routing policy.
How should security impact routing?
  Ideally: Prefer secure routes over all others
  Reality: Cost (business relationship) and path length may be preferred over security.
security
cost & performance
Our strategy doesn't require prioritizing security
over economics or path length

## Slide 13: Challenges to S*BGP deployment
RPKI is a necessity – now on the horizon!
Incentives for deployment?
We’ve seen similar problems before:
Spread of innovations in social networks [Morris 2001, Kempe et al. 2003]
  Nodes adopt innovations when local utility exceeds a threshold
  Utility only depends on immediate neighbors!
  Network protocol adoption [Ratnasamy et al. 2005]
  Client demand for innovation creates financial incentive
  Relied on additional mechanisms to route traffic to upgraded networks
S-BGP adoption [Chang et al. 2006]
  Assumed security benefits would be sufficient incentive
  Security is an intangible benefit

## Slide 14: Overview
S*BGP will necessarily go through a transition phase
How should deployment occur?
Our Goal: Come up with a strategy for S*BGP (S-BGP/soBGP) deployment.
How governments & standards groups invest resources
To enable a small set of ASes to create market pressure…
…and drive voluntary deployment by many other ASes!
Measure of success: number of ASes deploying S*BGP
Does not quantify security improvement.
We are currently working to quantifying the security during partial deployment.

## Slide 15: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 16: How to deploy S*BGP globally?
Pessimistic view:
No local economic incentives; only security incentives
Like IPv6, but worse, because entire path must be secure.
Our view:
S*BGP has an advantage: it affects route selection
  Even if it comes after cost and length in decision process.
This can drive traffic towards ISPs deploying S*BGP
ISPs want to attract more traffic destined to customers
Even if they don’t care about security!
ISPs would be the ones forced to upgrade all of their equipment to support this initiative, but how would it benefit them? As commercial companies, if there is little to no benefit (potential to increase profit), why would they implement a potentially costly solution? The answer is they won’t.
[http://www.omninerd.com/articles/Did_China_Hijack_15_of_the_Internet_Routers_BGP_and_Ignorance]

## Slide 17: Our Strategy: 3 Guidelines for Deploying S*BGP (1)
Secure ASes should break ties in favor of secure paths
Sprint
Equally good paths to the destination?
(in terms of cost and path length)
Pick the secure one!

## Slide 18: How this creates incentives
  ISP
  ISP
8359
Sprint
18608
13789
18608
38.101.185.0/24
8359, 18608
38.101.185.0/24
18608
38.101.185.0/24
13789, 18608
38.101.185.0/24
ISPs can use S*BGP to attract customer traffic & thus money
$
$
  AS 8359 delivers more traffic to his customer
Sprint needs to break the tie between equally good paths.

## Slide 19: How this creates incentives
  AS 8359 delivers less traffic to his customer
8359
Sprint
18608
18608
38.101.185.0/24
8359, 18608
38.101.185.0/24
13789
$
$
13789: (18608, 38.101.185.0/24)
13789: (18608, 38.101.185.0/24)
Sprint: (13789, 18608, 38.101.185.0/24)
ISPs can use S*BGP to attract customer traffic & thus money
Sprint uses security to break the tie!

## Slide 20: Our Strategy: 3 Guidelines for Deploying S*BGP (1)
Secure ASes should break ties in favor of secure paths
Cheap S*BGP for stubs (e.g., simplex S*BGP)
ISP1
Boston U
Bank of A
A stub is an AS that has no customers.
85% of ASes are stubs!
Boston U
Bank of A

## Slide 21: Simplex S*BGP: Cheap S*BGP for Stubs
A stub never transits traffic
Only announces its own prefixes..
…and receives paths from provider
Sign but don’t verify!
(rely on provider to validate)
2 options for deploying S*BGP in stubs:
Have providers sign for stub customers. (Stubs do nothing)
Stubs run simplex S*BGP. (Stub only signs, provider validates)
  No hardware upgrade required
    Sign for own prefixes, not ~300K prefixes
    Use ~1 private key, not ~36K public keys
  Security impact is minor (we evaluated this):
    Stub vulnerable to attacks by its direct provider.
18608
  Stub
18608
38.101.185.0/24
X

## Slide 22: Our Strategy: 3 Guidelines for Deploying S*BGP (2)
Secure ASes should break ties in favor of secure paths
Cheap S*BGP for stubs (e.g., simplex S*BGP)
(possibly with some government subsidies)
Initially, we need a few early adopters deploy S*BGP. (gov’t incentives, PR, concern for security, etc).
Who should these ASes be?
ISP1
Boston U
Bank of A

## Slide 23: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 24: Model: S*BGP deployment process
Initial state:
  Early adopter ASes have deployed S*BGP
  Their stub customers deploy simplex S*BGP
Each round with state S:
  Compute utility for each ISP n given state S
  … and S with ISP n deploying S*BGP
  If utility increases enough ISP n chooses to deploy S*BGP
Termination:
  Process continues until no new ISP wants to change their deployment decision
ISP n
ISP n
ISP n

## Slide 25: How do we compute ISP utility? (1)
    Customer traffic thru ISP n to dest d
    Utilityn(S) = ∑
all dests
Important Note: ISP utility does not depend on security.
Captures the idea that:
ISPs profit by transiting traffic
to their customers
i.e., Weighted sum of source ASes
routing through ISP n (on all edges)
to customers only.
$
$
ISP n
$
customers
traffic

## Slide 26: How do we compute ISP utility? (2)
  Let S be the state of the network (i.e. who deploys S*BGP)
  Can compute utility if we know S and ASes' routing policies
    Customer traffic thru ISP n to dest d
    Utilityn(S) = ∑
all dests
Ranking function:
1. Prefer customer paths
over peer paths
over provider paths
2. Prefer shorter paths
3. If secure, prefer secure paths
.
4. Arbitrary tiebreak
Export Policy:
Export customer path
  to all neighbors.
Export peer/provider path
to all customers.

## Slide 27: Our Model: ISP S*BGP Decision Rule
  An ISP deploys S*BGP if it increases its utility by θ %
  Let S be the state of the network (i.e. who deploys S*BGP)
  ISP n decides to deploy iff
  Utilityn (S with n deploying) > (1 + θ ) Utilityn(S)
θ is the deployment threshold,
Models % profit that is reinvested in S*BGP deployment
When an ISP deploys, it deploys simplex S*BGP in all its stubs.
ISP n

## Slide 28: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 29: Simulations Overview
Large scale simulations! Each round, we compute:
Paths between all pairs of ASes O(n2)
  once for each ISP O(n) (to evaluate revenue increase)
  Each iteration: O(n3) !
Run over the entire AS level topology, n=36,000
Custom algorithms, parallelized on 200-node DryadLINQ cluster
Many simulations run to understand robustness
Early adopter sets
Deployment thresholds θ
Traffic sourced by content providers
AS Graphs [UCLA Cyclops + IXP] + Augmented topology

## Slide 30: Case Study of S*BGP deployment
Ten early adopters:
Five Tier 1s:
  Sprint (AS 1239)
  Verizon (AS 701)
  AT&T (AS 7018)
  Level 3 (AS 3356)
  Cogent (AS 174)
The five content providers source 10% of Internet traffic
Stubs break ties in favor of secure paths
Threshold θ = 5%.
Five Popular Content Providers
  Google (AS 15169)
  Microsoft (AS 8075)
  Facebook (AS 32934)
  Akamai (AS 22822)
  Limelight (AS 20940)
This leads to 85% of ASes deploying S*BGP
(65% of ISPs)

## Slide 31: Simulation: Market pressure drives deployment (1)
Round 0
13789
Sprint
8359
18608
13789
18608
8359
Round 1
Round 4
  Stub

## Slide 32: Simulation: Market pressure drives deployment (2)
Round 4
Sprint
8359
8342
30733
6731
50197
13789
18608
6731
50197
Round 5
  Stub
  Stub

## Slide 33: Simulation: Market pressure drives deployment (3)
Sprint
8359
8342
30733
6731
50197
13789
18608
6731
50197
8342
41209
9002
43975
39575
Round 6
41209
39575
Round 7
  Stub
  Stub
  Stub

## Slide 34: Changes in Utility as Deployment Progresses (1)
Sprint
8359
8342
30733
6731
50197
6731
50197
Let’s zoom in on utility of each of these three ISPs…

## Slide 35: Changes in Utility as Deployment Progresses (2)
round
ASes that deploy see initial gains
But return to approx.
their original utility
ASes that do not deploy cannot gain traffic

## Slide 36: Tiebreak Sets: The Source of Competition (1)
13789
Sprint
8359
18608
Sprint’s tiebreak set to destination AS18608 is
{AS 13789, AS 8359}
Thus, these two ISPs compete for traffic!

## Slide 37: Tiebreak Sets: The Source of Competition (2)
Average tiebreak set size is tiny = 1.18 !
We also get ~same results (not shown)
if only ISPs break ties on secure paths (i.e., 15% of ASes)
 Global deployment even if 96% of routing decisions are unaffected by security.
80% of tiebreak sets have only 1 path!

## Slide 38: So who should be the early adopters?
Small target set suffices for small threshold
Higher threshold
requires a larger target set.
Theorem: Finding the optimal set of early adopters is NP-hard. Approximating this within a constant factor is also NP-hard.

## Slide 39: Simplex S*BGP vs. Market-pressure
Market pressure
Few ISPs on.
Most adoption via
Simplex S*BGP
Turning on just
the content providers
doesn’t do much!

## Slide 40: The Content Providers (CP) as early adopters?
  Cyclops AS graph has poor visibility into CP connectivity
  CP degree ~10x less than degree of largest Tier 1 ISP
  We augment graph so CP degree ≈ Tier 1 degree
  CP average path lengths drop from 3.5 to about 2.1
  How much traffic is sourced by the 5 CPs?
  Sweep through values x = {10%, 20%, 33%, 50%}
  Tier 1s are usually more influential early adopters…
  except if x is large (>33%) and threshold θ is small (<15%)
  Why? Tier 1s still transit more traffic than the CPs source,
  … and can leverage simplex S*BGP

## Slide 41: Outline
Part 1: Background
Part 2: Our strategy
Part 3: Evaluating our strategy
  Model
  Simulations
Part 4: Summary and recommendations

## Slide 42: Summary and Recommendations
  How to create a market for S*BGP deployment?
  Market pressure via S*BGP influence on route selection.
  Many secure destinations via simplex S*BGP.
  Where should government incentives and regulation go?
  Focus on early adopters; Tier 1s, maybe content providers
  Subsidize ISPs to upgrade stubs to simplex S*BGP
  Other challenges and future work :
  ISPs need tools to predict S*BGP impact on traffic
    How to handle traffic shifts?
  BGP and S*BGP will coexist in the long run
    What does this mean for security?

## Slide 43
  Contact: phillipa@cs.toronto.edu
  http://www.cs.toronto.edu/~phillipa/sbgpTrans.html
  Thanks to Microsoft Research SVC and New England for supporting us with DryadLINQ.

## Slide 44: Data Sources for ChinaTel Incident of April 2010
Example topology derived from Routeviews messages observed at the LINX Routeviews monitor on April 8 2010
  BGP announcements & topology was simplified to remove prepending
  We anonymized the large ISP in the Figure.
  Actual announcements at the large ISP were:
  From faulty ChinaTel router: “4134 23724 23724 for 66.174.161.0/24”
  From Level 3: “3356 6167 22394 22394 for 66.174.161.0/24”
Traffic interception was observed by Renesys blog
  http://www.renesys.com/blog/2010/11/chinas-18-minute-mystery.shtml
  We don’t have data on the exact prefixes for which this happened.
AS relationships: inferred by UCLA Cyclops