## Slide 1: Cloud Computing inside Virtualized Datacenters
V. Arun
College of Computer Science
University of Massachusetts Amherst

## Slide 2: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 3
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Internet
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 4
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 5: Key broad questions
How are massive numbers of commodity machines networked inside a data center?
Virtualization: How to effectively manage physical machine resources across client virtual machines?
How to reduce major capital and operational costs:
  Server equipment
  Power and cooling
  Power and cooling
This lab: mainly gain some insights into the second question.

## Slide 6: Common cloud computing models
Service models:
  IaaS: Infrastructure as a Service (e.g., Amazon EC2, Microsoft Azure, Google Compute Engine)
  PaaS: Platform as a Service (e.g., Google AppEngine)
  SaaS: Software as a Service (Office360, Amazon DynamoDB)
Management:
  Public clouds: Utility model, shared hardware, no control of hardware, self-managed (AWS, Azure, GCE)
  Private clouds: More isolated (secure?), federal compliance, customizable hardware, customizable hardware sharing

## Slide 7: OpenStack: A cloud OS for private clouds
OpenStack is a cloud operating system that controls large pools of compute, storage, and networking resources throughout a datacenter, all managed through a dashboard that gives administrators control while empowering their users to provision resources through a web interface.

## Slide 8: OpenStack UI

## Slide 9: Where Contrail fits in
OpenContrail plugs into OpenStack’s networking component (Neutron)

## Slide 10: Contrail system overview

## Slide 11: Contrail nodes
Configuration nodes: persistent configuration state
Control nodes: keeps ephemeral network state and and effects logically centralized control plane
Analytics nodes: Statistics from network elements
Compute nodes: General-purpose virtualized servers
Gateway nodes: Physical routers connecting tenant to external networks
Service nodes: Forwarding plane services (deep packet inspection, intrusion detection, WAN bandwidth optimizers, etc.) or “NFVs”

## Slide 12: Internal structure of compute node

## Slide 13: vRouter functions
vRouter agent
  Exchanging control state
  Receiving low-level config state
  Reporting analytics, installing forwarding state
  Proxying DHCP, ARP, DNS, etc.
vRouter forwarding plane
  Encapsulating to-overlay packets and decapsulating from-overlay packets
  Assigning packets to routing instance based on VNI
  Implementing forwarding policy rules

## Slide 14: vRouter forwarding plane internals

## Slide 15: Control nodes
Receive config state from configuration nodes (IF-MAP)
Exchange routes with each other using IBGP
Exchange routes with vRouters (XMPP)
Exchange routes with external gateways using BGP

## Slide 16: Control node internals
Network control protocol is BGP (not OpenFlow but analogous)

## Slide 17: Configuration node functions
REST API for north-bound interface to OpenStack
Cassandra key-value store for persistent config storage
Schema transformer (high-level to low-level)
ZooKeeper for transactions to assign unique IDs

## Slide 18: Configuration node

## Slide 19: Multi-tenancy

## Slide 20: Service chaining

## Slide 21: This lab
Familiarization with OpenStack and OpenContrail UIs
Create simple virtual networks with virtual servers and virtual routers
Create simple multi-tenant networks
Understand MPLS based tunneling mechanism for setting up flow rules
Understand virtualization, isolation, load balancing
Use tools like glance to load VM images

## Slide 22: Virtual Circuits and MPLS tunneling

## Slide 23: Connection, connection-less service
datagram network (Internet) provides network-layer connectionless service
virtual-circuit network (ATM) provides network-layer connection service
analogous to TCP/UDP connecton-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: primarily in network core

## Slide 24: Virtual circuits (e.g., ATM)
call setup, teardown for each call before data can flow
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
source-to-dest path behaves like telephone circuit
  performance-wise
  network actions along source-to-dest path

## Slide 25: Virtual circuit implementation
VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number typically changed on each link.
  new VC number comes from forwarding table

## Slide 26: Virtual circuit forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!

## Slide 27: Virtual circuit signaling
application
transport
network
data link
physical
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical
How does this compare to datagram networks like the Internet?

## Slide 28: Datagram networks (e.g., Internet)
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 29: Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 30: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 31: Multiprotocol label switching (MPLS)
initial goal: high-speed IP forwarding using fixed length label (instead of IP address)
  fast lookup using fixed length identifier (rather than longest prefix matching)
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
5

## Slide 32: MPLS capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)

## Slide 33: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4

## Slide 34: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and dest. address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address

## Slide 35: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
D
R4
R5
A
R6
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
modified
link state
flooding
RSVP-TE

## Slide 36: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1